## Slide 1: IAS Machine

## Slide 2
Organization of the von Neumann machine
IAS – a prototype developed by John Von Neumann in 1946 at Princeton
University. (Institute for Advanced Study)
Structure of Von Neumann machine(IAS Computer)
Notes: IAS: Institute for Advanced Studies.

## Slide 3
IAS – memory format
1000 x 40 bit words ( 1000 storage locations of 40 binary bits each)
  Binary number( both data and instructions are stored here)
Number Format:
  Each number is represented by a sign bit and a 39 bit value.
Instruction Format:
  A word may contain 20 bit instruction with each instruction consisting of an 8 bit operation code (opcode) specifying the operation to be performed and a 12 bit address designating one of the words in memory (0 to 999)

## Slide 4
IAS – Contd..
Memory Formats
1000 x 40 bit words ( 1000 storage locations of 40 binary bits each)
  Binary number( both data and instructions are stored here)
Number Format
  Each number is represented by a sign bit and a 39 bit value.
  Instruction Format
  - 20-bit instruction, 8-bit operation code (opcode)
  -12-bit address

## Slide 5: IAS – Contd..
IAS – Total 21 Instructions
  Data Transfer
  Unconditional Branch Instruction
  Conditional Branch Instruction
  Arithmetic
  Address Modify Instruction

## Slide 6
Expanded Structure of IAS

## Slide 7
Expanded structure of IAS computer
Set of registers (storage in CPU)
  Memory Buffer Register (MBR)
    Contains a word to be stored in memory or sent to the I/O unit, or it is used to receive a word from memory or from the I/O unit.
  Memory Address Register (MAR)
    Specifies the address in memory of the word to be written from or read into the MBR.
  Instruction Register (IR)
    Contains the 8 bit opcode instruction being executed.
  Instruction Buffer Register (IBR)
    Employed to hold temporarily the right hand instruction from a word in memory
  Program Counter (PC)
    Contains the address of the next instruction pair to be fetched from memory
  Accumulator (AC) & Multiplier Quotient (MQ)
    Employed to hold temporarily the right hand instruction from a word in memory. For eg. The result of multiplying two 40 bit numbers is an 80 bit number, the most significant 40 bits are stored in the AC and the least significant in the MQ.

## Slide 8
AC
MQ
Arithmetic & Logic Circuits
MBR
IBR
IR
Control
Circuits
PC
MAR
Input/output
Equipments
Main Memory
IAS Operation - Flowchart
MARPC
MBRM[MAR]
IRMBR<0..7>
MARMBR<8..19>
IBRMBR<20..39>
ACMBR
MBRM[MAR]
IRIBR<0..7>
MARIBR<8..19>
PCPC+1
PCMAR
MBRM[MAR]
Is next instruction in IBR?
No
yes
AC MBR

## Slide 9
AC
MQ
IBR
PC = 1
IR
MAR = 1
MEMORY
1. LOAD M(X) 500, ADD M(X) 501
2. STOR M(X) 500, (Other Ins)
.....
3
4
PC
MBR
IR
IBR
MAR
1
1
LOAD M(X) 500, ADD M(X) 501
AC
ADD M(X) 501
LOAD M(X)
500
3
ADD M(X)
501
2
4
2
STOR M(X) 500, (Other Ins)
(Other Ins)
STOR M(X)
500
3
7
MBR
Mar ← PC
add = 1
LOAD M(X) 500, ADD M(X) 501
ADD M(X) 501
LOAD M(X)
500
MAR =500
add = 500
MBR = 3
3
AC = 3
Add M(X)
501
MAR = 501
add = 501
PC = 2
4
MBR = 4
AC = 7
MAR ←PC
MAR = 2
add = 2
STOR M(X) 500, (Other Ins)
STOR M(X)
(Other Ins)
500
MAR = 500

## Slide 10: Register transfer operation for addition operation
1. LOAD M(X) 500, ADD M(X) 501
Register transfer operations: (PC = 1)
  MAR ← PC
  MBR ← M[MAR]
  IBR ← MBR[20:39]
  IR ← MBR[0:7]
  MAR ← MBR[8:19]
  MBR ← M[MAR]
  AC ← MBR
  IR ← IBR[0:7]
  MAR ← IBR[8:19]
  MBR ← M[MAR]
  AC ← AC + MBR

## Slide 11: Fetch / Execute Cycle

## Slide 12
AC
MQ
IBR
PC = 1
IR
MAR = 1
MEMORY
1. LOAD M(X) 500, ADD M(X) 501
2. STOR M(X) 500, (Other Ins)
.....
3
4
PC
MBR
IR
IBR
MAR
1
1
LOAD M(X) 500, ADD M(X) 501
AC
ADD M(X) 501
LOAD M(X)
500
3
ADD M(X)
501
2
4
2
STOR M(X) 500, (Other Ins)
(Other Ins)
STOR M(X)
500
3
7
MBR
Mar ← PC
add = 1
LOAD M(X) 500, ADD M(X) 501
ADD M(X) 501
LOAD M(X)
500
MAR =500
add = 500
MBR = 3
3
AC = 3
Add M(X)
501
MAR = 501
add = 501
PC = 2
4
MBR = 4
AC = 7
MAR ←PC
MAR = 2
add = 2
STOR M(X) 500, (Other Ins)
STOR M(X)
(Other Ins)
500
MAR = 500

## Slide 13
Notes: Note: This is an instruction cycle state diagram without interrupts

## Slide 14
Instruction set: Collection of instructions that the CPU can execute
What an Instruction set should specify?
Which Operation to perform (Opcode)
Where to find the operand or operands (CPU registers, main memory or I/O port)
Where to put the result, if there is result
Where to find the next instruction

## Slide 15: IAS Instruction set

## Slide 16: IAS Instruction set Contd..

## Slide 17: Instruction Format
The instruction is divided into two fields
  Opcode field
  Operand field
This operand field further divided into one to four fields.
Simple instruction format
Opcode
Operand
Address1
Operand
Address2
Result
Address1
Next
Instruction

## Slide 18
Instruction Set is categorized into types based on
  Operation performed
  number of operand addresses
  and addressing modes
Based on Operation
Data Movement
  Memory : LOAD, STORE, MOV I\O Instructions: IN, OUT
Data Processing
  Arithmetic : Add, Sub, MUL Logic Instructions: AND, OR,
Control Instructions
  Conditional : JNZ, JZ Un Conditional: Jump

## Slide 19
Based on number of operand address in the instruction.
    4 Address Instruction
    3 Address Instruction
    2 Address Instruction
    1 Address Instruction
    0 Address Instruction
For a two-operand arithmetic instruction, five items need to be specified
  Operation to be performed (opcode)
  Location of the first operand
  Location of the second operand
  Place to store the result
  Location of next instruction to be executed

## Slide 20: Assumptions 24-bit memory address (3 bytes) 128 instructions (7 bits rounded to 1 byte)

## Slide 21: 4- Address Instruction
24 Bits / 3 Bytes
Memory
Op Code
ResAddr
Op1Addr
Op2Addr
NextiAddr
8
24
24
24
24
+
CPU
Op Code
ResAddr
Op1Addr
Op2Addr
NextiAddr
Op1
Op2
Resop
Example: add M1,M2,M3, nexti
M(1)M(2)+M(3)
Memory Required to store an Instruction:
5 x 3 bytes = 15 Bytes
Memory Required to Encode an Instruction:
1Byte+ 4 x 3 bytes = 13 Bytes
Calculation of Memory Accesses
To fetch Instruction itself
Opcode=1
Op1Addr=1
Op2Addr=1
ResAddr=1
NextiAddr=1
Total=5
To Execute an Instruction
Op1=1
Op2=1
Res=1
Total=3
Total Memory Traffic= No. of M/A to fetch + No. of M/A to Execute
Total Memory Traffic= 5 + 3 =8

## Slide 22: 3- Address Instruction
24 Bits / 3 Bytes
Memory
Op Code
ResAddr
Op1Addr
Op2Addr
8
24
24
24
+
CPU
Op Code
ResAddr
Op1Addr
Op2Addr
Op1
Op2
Resop
Example: add M1,M2,M3
M(1)M(2)+M(3)
Memory Required to store an Instruction:
4 x 3 bytes = 12 Bytes
Memory Required to Encode an Instruction:
1Byte+ 3 x 3 bytes = 10 Bytes
Calculation of Memory Accesses
To fetch Instruction itself
Opcode=1
Op1Addr=1
Op2Addr=1
ResAddr=1
Total=4
To Execute an Instruction
Op1=1
Op2=1
Res=1
Total=3
Total Memory Traffic= No. of M/A to fetch + No. of M/A to Execute
Total Memory Traffic= 4+ 3 =7
PC
24

## Slide 23: 2- Address Instruction
24 Bits / 3 Bytes
Memory
Op Code
Op1Addr
Op2Addr
8
24
24
24
+
CPU
Op Code
Op1Addr
Op2Addr
Op1
Op2
Resop
Example: add M2,M3
M(2)M(2)+M(3)
Memory Required to store an Instruction:
3 x 3 bytes = 09 Bytes
Memory Required to Encode an Instruction:
1Byte+ 2 x 3 bytes = 7 Bytes
Calculation of Memory Accesses
To fetch Instruction itself
Opcode=1
Op1Addr=1
Op2Addr=1
Total=3
To Execute an Instruction
Op1=1
Op2=1
Res=1
Total=3
Total Memory Traffic= No. of M/A to fetch + No. of M/A to Execute
Total Memory Traffic= 3+ 3 =6
PC
24

## Slide 24: 1- Address Instruction
24 Bits / 3 Bytes
Memory
Op Code
Op1Addr
8
24
24
+
CPU
Op Code
Op1Addr
Op1
Op2
Resop
Example: add M2
Memory Required to store an Instruction:
2 x 3 bytes = 06 Bytes
Memory Required to Encode an Instruction:
1Byte+ 1 x 3 bytes = 4Bytes
Calculation of Memory Accesses
To fetch Instruction itself
Opcode=1
Op1Addr=1
Total=2
To Execute an Instruction
Op1=1
Total=1
Total Memory Traffic= No. of M/A to fetch + No. of M/A to Execute
Total Memory Traffic= 2+ 1 =3
PC
24
Acc

## Slide 25: 0-Address Instruction

## Slide 26: Comparisons
Instruction Type | Memory To Store in Bytes | Memory To Encode in Bytes | M/As to fetch an Instruction | M/As to Execute an Instruction | Memory Traffic
4-address | 5 x 3 = 15 | 1+(4 x 3) = 13 | 5 | 3 | 5+3=8
3-Address | 4 x 3 = 12 | 1+(3 x 3) = 10 | 4 | 3 | 4+3=7
2-Address | 3 x 3 = 09 | 1+(2 x 3) = 07 | 3 | 3 | 3+3=6
1-Address | 2 x 3 = 06 | 1+(1 x 3) = 04 | 2 | 1 | 2+1=3
0-Address | 1 x 3 = 03 | 1+(0 x 3) = 01 | 1 | 0 | 1+0=1

## Slide 27: Evaluate a = (b+c)*d - e
ab+c
add a, b, c
mpy a, a, d
sub a, a, e
aa*d
aa-e
ab
load a, b
add a, c
mpy a, d
aa+c
aa*d
sub a, e
aa-e
Accb
load b
add c
mpy d
AccAcc+c
AccAcc*d
sub e
AccAcc-e
store a
aAcc
push b
push c
add
push d
mpy
push e
sub
pop a
3-Address
2-Address
1-Address
0-Address

## Slide 28
ab+c
add a, b, c
mpy a, a, d
sub a, a, e
aa*d
aa-e
ab
load a, b
add a, c
mpy a, d
aa+c
aa*d
sub a, e
aa-e
Memory to Store | Memory to encode | M/As to Fetch | M/As to Execute | Memory Traffic
4*3=12 | 1+(3*3)=10 | 4 | 3 | 4+3=7
4*3=12 | 1+(3*3)=10 | 4 | 3 | 4+3=7
4*3=12 | 1+(3*3)=10 | 4 | 3 | 4+3=7
36 | 30 | 12 | 9 | 21
Memory to Store | Memory to encode | M/As to Fetch | M/As to Execute | Memory Traffic
3*3=9 | 1+(2*3)=7 | 3 | 2 | 3+2=5
3*3=9 | 1+(2*3)=7 | 3 | 3 | 3+3=6
3*3=9 | 1+(2*3)=7 | 3 | 3 | 3+3=6
3*3=9 | 1+(2*3)=7 | 3 | 3 | 3+3=6
36 | 28 | 12 | 11 | 23

## Slide 29
Accb
load b
add c
mpy d
AccAcc+c
AccAcc*d
sub e
AccAcc-e
store a
aAcc
Memory to Store | Memory to encode | M/As to Fetch | M/As to Execute | Memory Traffic
2*3=6 | 1+(1*3)=4 | 2 | 1 | 2+1=3
2*3=6 | 1+(1*3)=4 | 2 | 1 | 2+1=3
2*3=6 | 1+(1*3)=4 | 2 | 1 | 2+1=3
2*3=6 | 1+(1*3)=4 | 2 | 1 | 2+1=3
2*3=6 | 1+(1*3)=4 | 2 | 1 | 2+1=3
30 | 20 | 10 | 5 | 15
6 | 4 | 2 | 1 | 3
3 | 1 | 1 | 0 | 1
39 | 23 | 13 | 5 | 18
push b
push c
add
push d
mpy
push e
sub
pop a

## Slide 30
Evaluate X=(A+B) * (C+D)
Evaluate Y=(A-B)/[C+(D/E)]

## Slide 31: References
Reference Book
W. Stallings, Computer organization and architecture, Prentice-Hall,2000
J. P. Hayes, Computer system architecture, McGraw Hill,2000
Vincent .P. Heuring, Harry F. Jordan “ Computer System design and Architecture” Pearson, 2nd Edition, 2003