## Slide 1: Fundamentals of AC Circuits
Module 2: Fundamentals of AC Circuits

## Slide 2: Introduction to AC Circuits
Electrical appliances in the house use alternating current (AC) circuits.

## Slide 3: Direct Current (DC) and Alternating Current (AC)
When a current is constant with time, we say that we have direct current, abbreviated as dc
When current that varies with time, reversing direction periodically, is called alternating current, abbreviated as ac.
?

## Slide 4: Direct Voltage (DC) and Alternating Voltage (AC)
The voltage associated with a circuit element is the energy transferred per unit of charge that flows through the element.
The units of voltage are volts (V), which are equivalent to joules per coulomb (J/C).
Voltage constant with time is called dc voltage.
Voltage that change in magnitude and alternate in polarity with time is called ac voltage.

## Slide 5: Sinusoidal AC Voltage
A sinusoidal voltage is shown in Figure, and is given by
Here, is the peak value of the voltage.
is the angular frequency in radians per second
is the phase angle
Sinusoidal signals are periodic, repeating the same pattern of values in each period T.
The frequency of a periodic signal is the number of cycles completed in one second. Thus, we obtain
The units of frequency are hertz (Hz).
is the angular frequency in radians per second.

## Slide 6: Root-Mean-Square Values
Consider applying a periodic voltage v(t) with period T to a resistance R. The power delivered to the resistance is given by
Furthermore, the energy delivered in one period is given by
The average power delivered to the resistance is the energy delivered in one cycle divided by the period. Thus,

## Slide 7: Root-Mean-Square (RMS) Values of Voltage
This can be rearranged as
Now, we define the root-mean-square (rms) value of the periodic voltage v(t) as

## Slide 8: RMS Value of Current
Similarly for a periodic current i(t), we define the rms value as
The average power delivered if i(t) flows through a resistance is given by

## Slide 9: overview
After Substituting v(t) in
Similarly,

## Slide 10: Ex 1: Power Delivered to a Resistance by a Sinusoidal Source
Suppose that a voltage given by v(t)=100cos(100wt)V is applied to a 50Ω resistance.
Sketch v(t) to scale versus time.
Find the rms value of the voltage and the average power delivered to the resistance.
Find the power as a function of time and sketch to scale

## Slide 11: Ex 2 : Power Delivered to a Resistance by a Sinusoidal Source
Suppose that a sinusoidal voltage is given by
v(t) = 150 cos(200πt - 30°) V
Find the angular frequency, the frequency in hertz, the period, the peak value, and the rms value.
If this voltage is applied to a 50Ω resistance, compute the average power delivered.
Sketch v(t) to scale versus time

## Slide 12: Fundamentals of AC Circuits
Module 2: Fundamentals of AC Circuits

## Slide 13: sinusoidal steady-state analysis of Rl, RC & RLC Circuits

## Slide 14: overview

## Slide 15: Phasors
Here, we will see that sinusoidal steady-state analysis is greatly facilitated if the currents and voltages are represented as vectors (called phasors) in the complex-number plane.
We start with a study of convenient methods for adding (or subtracting) sinusoidal waveforms.
We often need to do this in applying Kirchhoff’s voltage law (KVL) or Kirchhoff’s current law (KCL) to ac circuits.
For example, in applying KVL to a network with sinusoidal voltages, we might obtain the expression
v(t) = 10 cos(ωt) + 5 sin(ωt + 60) + 5 cos(ωt + 90)
To obtain the peak value of v(t) and its phase angle, v(t) = Vm cos(ωt + θ)

## Slide 16: Phasor Definition
For a sinusoidal voltage of the form,
We define phasor as
If the sinusoid is of the form
we first convert to a cosine function by using the trigonometric identity
Thus, we have
and the phasor is

## Slide 17: Phasor Definition
Phasors are obtained for currents in a similar fashion.
Thus, for the currents
Conversion of Phasor form to Complex form
 V=v(cos()+j sin())
Conversion of Complex to Phasor
v = a + jb 

## Slide 18: Adding Voltages Using Phasors
v(t) = 10 cos(ωt) + 5 sin(ωt + 60) + 5 cos(ωt + 90)
Step 1: Convert to a cosine function by using the trigonometric identity
v(t) = 10 cos(ωt) + 5 cos(ωt + 60 - 90) + 5 cos(ωt + 90)
v(t) = 10 cos(ωt) + 5 cos(ωt - 30) + 5 cos(ωt + 90)
Step 2: Represent in phasor form using phasor definition
v(t)
Step 3: Convert Phasor form to Complex form
v(t) = 10 (cos(0)+j sin(0)) + 5 (cos(-30)+j sin(-30)) + 5 (cos(90)+j sin(90))
v(t) = 10 (1 + j0) + 5 (0.866 – j0.5) + 5 (0 + j1)
v(t) = 14.33 + j2.5

## Slide 19: Adding Voltages Using Phasors
Step 4: Convert Phasor form to Complex form
v(t) = 10 (cos(0)+j sin(0)) + 5 (cos(-30)+j sin(-30)) + 5 (cos(90)+j sin(90))
v(t) = 10 (1 + j0) + 5 (0.866 – j0.5) + 5 (0 + j1)
v(t) = 14.33 + j2.5
Step 5: Convert Complex form to Phasor form
v(t) = = 14.54
Step 6: Convert Phasor form to sinusoidal form
v(t) = 14.54 cos (ωt + 9.89)

## Slide 20: Example 1: Using Phasors to Add Sinusoids
Suppose that,
v1(t) = 20 cos(ωt − 45◦)
v2(t) = 10 sin(ωt + 60◦)
Reduce the sum vs(t) = v1(t) + v2(t) to a single term.

## Slide 21: Example 2: Reduce the following expressions by using phasors
v1(t) = 10 cos(ωt) + 10 sin(ωt)
i1(t) = 10 cos(ωt + 30◦) + 5 sin(ωt + 30◦)
i2(t) = 20 sin(ωt + 90◦) + 15 cos(ωt − 60◦)

## Slide 22: Fundamentals of AC Circuits
Module 2: Fundamentals of AC Circuits

## Slide 23: overview

## Slide 24: Phasor Definition
For a sinusoidal voltage of the form,
We define phasor as
If the sinusoid is of the form
we first convert to a cosine function by using the trigonometric identity
Thus, we have
and the phasor is

## Slide 25: Phasor Definition
Phasors are obtained for currents in a similar fashion.
Thus, for the currents
Conversion of Phasor form to Complex form
 V=v(cos()+j sin())
Conversion of Complex to Phasor
v = a + jb 

## Slide 26: Complex impedances - Inductance
Consider an inductance in which the current is a sinusoid given by
Recall that the voltage across an inductance is
Substituting into and reducing, we obtain
Now, the phasors for the current and voltage are
Current lags voltage by 90° in a pure inductance.

## Slide 27
can we rewritten as
We refer to the term as the impedance of the inductance and denote it as .
Overview
Current lags voltage by 90° in a pure inductance.

## Slide 28: Complex impedances - Capacitance
In a similar fashion for a capacitance, we can show that if the current and voltage are sinusoidal, the phasors are related by
in which the impedance of the capacitance is
Suppose that the phasor voltage is
Then, the phasor current is
Current leads voltage by 90° in a pure capacitance

## Slide 29: Complex impedances - Resistance
For a resistance, the phasors are related by
Because resistance is a real number, the current and voltage are in phase
For a pure resistance, current and voltage are in phase

## Slide 30: Overview
Inductance
Current lags voltage by 90° in a pure inductance.
Capacitance
Current leads voltage by 90° in a pure capacitance
Resistance
For a pure resistance, current and voltage are in phase

## Slide 31: Combining Impedances in Series and Parallel – Ex 1
Determine the complex impedance between terminals shown in Figure for
= 1000 rad/s

## Slide 32: Ex 2
A voltage vL(t) = 100 cos(200t) is applied to a 0.25-H inductance. (Notice that w = 200.)
a. Find the impedance of the inductance, the phasor current, and the phasor voltage.
b. Draw the phasor diagram.

## Slide 33: Ex 3
A voltage vC(t) = 100 cos(200t) is applied to a 100µF capacitance.
a. Find the impedance of the capacitance, the phasor current, and the phasor voltage.
b. Draw the phasor diagram.

## Slide 34: Circuit Analysis with Phasors And Complex impedances
Kirchhoff’s Laws
Node-Voltage Analysis
Mesh-Current Analysis

## Slide 35: Kirchhoff’s Laws
Steady-State AC Analysis of a Series Circuit
Find the steady-state current for the circuit shown in Figure. Also, find the phasor voltage across each element

## Slide 36: Fundamentals of AC Circuits
Module 2: Fundamentals of AC Circuits

## Slide 37: overview

## Slide 38: overview
 V=v(cos()+j sin())
v = a + jb 

## Slide 39: Overview
Inductance
Current lags voltage by 90° in a pure inductance.
Capacitance
Current leads voltage by 90° in a pure capacitance
Resistance
For a pure resistance, current and voltage are in phase

## Slide 40: Circuit Analysis with Phasors And Complex impedances
Kirchhoff’s Laws
Node-Voltage Analysis
Mesh-Current Analysis

## Slide 41: Kirchhoff’s Laws
Steady-State AC Analysis of a Series Circuit
Find the steady-state current for the circuit shown in Figure. Also, find the phasor voltage across each element

## Slide 42: Node-voltage analysis
Use the node-voltage technique to find v1(t) and v2(t) in steady state for the circuit shown in Figure

## Slide 43: Mesh-current analysis
Solve for the mesh currents I1 and I2

## Slide 44: Assignment 1
Find Mesh Currents I1 and I2

## Slide 45: Assignment 2
Compute the complex impedance of the network shown in Figure for ω = 500. Repeat for ω = 1000 and ω = 2000. Give the answers in both polar and rectangular forms

## Slide 46: Ac POWER calculations

## Slide 47: Current, Voltage, and Power for a Resistive Load
Current, Voltage, and Power for a Inductive Load
Using trigonometric identity cos(x) sin(x) = (1/2) sin(2x)

## Slide 48: Current, Voltage, and Power for a Capacitive Load
Using trigonometric identity cos(x) sin(x) = (1/2) sin(2x)

## Slide 49: Power Calculations for a General Load
Now, let us consider the voltage, current, and power for a general RLC load for which the phase θ can be any value from −90◦ to +90◦. We have
Using and
Active Power & Units (W)

## Slide 50: Power Factor & reactive power
Power Factor (PF) = cos()
In general, the phase of the voltage may have a value other than zero. Then, θ should be taken as the phase of the voltage θv minus the phase of the current θi, or
θ = θv − θi
Reactive Power
Apparent Power = =

## Slide 51: Ac power calculations
Compute the power, reactive power and apparent power taken from the source for the circuit