## Slide 1: Module 3: Digital Systems

## Slide 2: 1. Number systems

## Slide 3: Number system
In digital electronics, the number system is used for representing the information.
The number system has different bases and the most common of them are the decimal, binary, octal, and hexadecimal.
The base of the number system is the total number of the digit used in the number system.
Suppose if the number system representing the digit from 0 – 9 then the base of the system is the 10.

## Slide 4: Types of Number Systems
Some of the important types of number system are
Decimal Number System
Binary Number System
Octal Number System
Hexadecimal Number System

## Slide 5: Decimal Number Systems
The number system is having digit 0, 1, 2, 3, 4, 5, 6, 7, 8, 9; this number system is known as a decimal number system because total ten digits are involved.
The base of the decimal number system is 10.

## Slide 6: Binary Number Systems
The modern computers do not process decimal number; they work with another number system known as a binary number system which uses only two digits 0 and 1.
The base of binary number system is 2 because it has only two digit 0 and 1.
The digital electronic equipment's are works on the binary number system and hence the decimal number system is converted into binary system.
Decimal | Binary
0 | 0000
1 | 0001
2 | 0010
3 | 0011
4 | 0100
5 | 0101
6 | 0110
7 | 0111
8 | 1000
9 | 1001
10 | 1010
11 | 1011
12 | 1100
13 | 1101
14 | 1110
15 | 1111

## Slide 7: Conversion of Decimal number to Binary Form
To convert a decimal number to binary, we repeatedly divide by two until the quotient is zero.
Then, the remainders read in reverse order give the binary form of the number.
Example 1: Convert the decimal number to binary.
Example 2: Convert the decimal number to binary.
Note: The decimal number is repeatedly divided by two. When the quotient reaches zero, we stop. Then, the binary equivalent is read as the remainders in reverse order

## Slide 8: Conversion of Binary to decimal Form
Example 3: Convert the binary number in the decimal form

## Slide 9: Octal Numbers
The base of a number system is equal to the number of digits used, i.e., for decimal number system the base is ten while for the binary system the base is two.
The octal system has the base of eight as it uses eight digits 0, 1, 2, 3, 4, 5, 6, 7.
All these digits from 0 to 7 have the same physical meaning as by decimal symbols, the next digit in the octal number is represented by 10, 11, 12, which are equivalent to decimal digits 8, 9, 10 respectively.
Decimal | Binary | Octal
0 | 0000 | 0
1 | 0001 | 1
2 | 0010 | 2
3 | 0011 | 3
4 | 0100 | 4
5 | 0101 | 5
6 | 0110 | 6
7 | 0111 | 7
8 | 1000 | 10
9 | 1001 | 11
10 | 1010 | 12
11 | 1011 | 13
12 | 1100 | 14
13 | 1101 | 15
14 | 1110 | 16
15 | 1111 | 17

## Slide 10: Hexadecimal Numbers
These numbers are used extensively in microprocessor work.
The hexadecimal number system has a base of 16, and hence it consists of the following sixteen number of digits.
0, 1, 2, 3, 4, 5, 6, 7, 8, 9, A, B, C, D, E, F.
Decimal | Binary | Octal | Hexadecimal
0 | 0000 | 0 | 0
1 | 0001 | 1 | 1
2 | 0010 | 2 | 2
3 | 0011 | 3 | 3
4 | 0100 | 4 | 4
5 | 0101 | 5 | 5
6 | 0110 | 6 | 6
7 | 0111 | 7 | 7
8 | 1000 | 10 | 8
9 | 1001 | 11 | 9
10 | 1010 | 12 | A
11 | 1011 | 13 | B
12 | 1100 | 14 | C
13 | 1101 | 15 | D
14 | 1110 | 16 | E
15 | 1111 | 17 | F

## Slide 11: Converting Octal and Hexadecimal to Binary
Decimal | Binary | Octal | Hexadecimal
0 | 0000 | 0 (000) | 0 (0000)
1 | 0001 | 1 (001) | 1 (0001)
2 | 0010 | 2 (010) | 2 (0010)
3 | 0011 | 3 (011) | 3 (0011)
4 | 0100 | 4 (100) | 4 (0100)
5 | 0101 | 5 (101) | 5 (0101)
6 | 0110 | 6 (110) | 6 (0110)
7 | 0111 | 7 (111) | 7 (0111)
8 | 1000 | 10 | 8 (1000)
9 | 1001 | 11 | 9 (1001)
10 | 1010 | 12 | A (1010)
11 | 1011 | 13 | B (1011)
12 | 1100 | 14 | C (1100)
13 | 1101 | 15 | D (1101)
14 | 1110 | 16 | E (1110)
15 | 1111 | 17 | F (1111)

## Slide 12: Converting Octal to Binary
Example 4: Convert the octal number to binary.
Note: In converting binary numbers to octal, we first arrange the bits in groups of three, starting from the binary point and working outward. If necessary, we insert leading or trailing zeros to complete the groups. Then, we convert each group of three bits to its octal equivalent.

## Slide 13: Convert Hexadecimal Numbers to Binary
Example 5: Convert the hexadecimal number to binary
Note: Conversion to hexadecimal uses the same approach, except that the binary number is arranged in groups of four bits.

## Slide 14: Converting Binary Numbers to Octal or Hexadecimal
Example 6: Convert 11110110 to octal and to hexadecimal.
Note: For conversion to octal, we first form three-bit groups, working outward from the binary point. Notice that we have appended leading and trailing zeros so that each group contains three bits. Next, we write the octal digit for each group.
Note: For conversion to hexadecimal, we form four-bit groups appending leading and trailing zeros as needed. Then, we convert each group to its equivalent hexadecimal integer.

## Slide 15: Assignment Q1
Convert the following binary numbers to decimal form
101
10101
1110
1101
1001
1111
Attach the photo
“Solution from Calculator”

## Slide 16: Assignment Q2
Express the following decimal numbers in binary form
7
9
6
11
63
67
Attach the photo
“Solution from Calculator”

## Slide 17: Assignment Q3
Express each of the following octal numbers in binary, decimal, and hexadecimal forms
Attach the photo
“Solution from Calculator”

## Slide 18: Assignment Q4
Express the following decimal numbers in binary, octal, and hexadecimal forms
313
253
349
835
212
Attach the photo
“Solution from Calculator”

## Slide 19: 2. Logic gates

## Slide 20: logic gates – Symbols & Truth Table
In this section, we consider circuits called logic gates that combine several logic variable inputs to produce a logic-variable output.
AND Gate
OR Gate
NOT Gate
NAND Gate
NOR Gate
XOR Gate

## Slide 21: AND Gate
The AND operation on two logic variables, A and B, is represented as AB, read as “A and B.”
The AND operation is also called logical multiplication.

## Slide 22: Three input and gate

## Slide 23: Or gate
The OR operation of logic variables is written as A+B, which is read as “A or B.”
Notice that A+B is 1 if A or B (or both) are 1.
The OR operation is also called logical addition.

## Slide 24: Three-input OR gate

## Slide 25: Not gate
The NOT operation on a logic variable is represented by placing a bar over the symbol for the logic variable. The symbol is read as “not A” or as “A inverse.” If A is 0, is 1, and vice versa.

## Slide 26: Nand gate
The NAND gate is equivalent to an AND gate followed by an inverter.
Notice that the symbol is the same as for an AND gate, with a bubble at the output terminal to indicate that the output has been inverted after the AND operation.
A | B | AND (AB) | NAND ()
0 | 0 | 0 | 1
0 | 1 | 0 | 1
1 | 0 | 0 | 1
1 | 1 | 1 | 0
A | B | AND (AB) | 
0 | 0 | 0 | 1
0 | 1 | 0 | 1
1 | 0 | 0 | 1
1 | 1 | 1 | 0

## Slide 27: Nor gate
Similarly, the NOR gate is equivalent to an OR gate followed by an inverter.
A | B | OR (A+B) | NOR ()
0 | 0 | 0 | 1
0 | 1 | 1 | 0
1 | 0 | 1 | 0
1 | 1 | 1 | 0
A | B | OR (A+B) | 
0 | 0 | 0 | 1
0 | 1 | 1 | 0
1 | 0 | 1 | 0
1 | 1 | 1 | 0

## Slide 28: Xor gate
The exclusive-OR (XOR) operation for two logic variables A and B is represented by A ⊕ B and is defined by
0 ⊕ 0 = 0
1 ⊕ 0 = 1
0 ⊕ 1 = 1
1 ⊕ 1 = 0
Notice that the XOR operation yields 1 if A is 1 or if B is 1, but yields 0 if both A and B are 1. The XOR operation is also known as modulo-two addition.
A | B | XOR
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
A⊕B = A+B

## Slide 29: Logic IC’s

## Slide 30: Example 1
Write a Boolean expression for the output of the logic circuit

## Slide 31: Example 2
Write a Boolean expression for the output of the logic circuit

## Slide 32: Example 3
Write a Boolean expression for the output of the logic circuit

## Slide 33: Example 4
Write a Boolean expression for the output of the logic circuit

## Slide 34: Example 5
Write a Boolean expression for the output of the logic circuit
Also give the truth table for the circuit

## Slide 35: Example 6
Write a Boolean expression for the output of the logic circuit
Also give the truth table for the circuit

## Slide 36: 3. Boolean Algebra
Postulates and Theorems

## Slide 37: Postulates
Assume A, B, and C are logical states that can have the values 0 (false) and 1 (true).
"+" means OR, "·" means AND, and [] means NOT A.
OR Operation | AND Operation | Law
A + 0 = A | A · 1 = A | Identity
A + = 1 | A · = 0 | Complement
A + B = B + A | A · B = B · A | Commutative Law
A + (B + C) = (A + B) + C | A · (B · C) = (A · B) · C | Associative Law
A + (B · C) = (A + B) · (A + C) | A · (B + C) = (A · B) + (A · C) | Distributive Law
OR Operation | AND Operation | Law
A + 0 = A | A · 1 = A | Identity
 |  | Complement
A + B = B + A | A · B = B · A | Commutative Law
A + (B + C) = (A + B) + C | A · (B · C) = (A · B) · C | Associative Law
A + (B · C) = (A + B) · (A + C) | A · (B + C) = (A · B) + (A · C) | Distributive Law

## Slide 38: Theorems
OR Operation | AND Operation | Theorem
A + A = A | A · A = A | Idempotent Law
A + 1 = 1 | A · 0 = 0 | Annulment Law
A + (A · B) = A | A · ( A + B) = A | Absorption law
A + ( · B) = A + B | A · ( + B) = A · B | Redundancy Law
(A · B) + ( · C) + (B · C) = (A · B) + ( · C) | A · (B + C) = (A · B) + (A · C) | Consensus Law
= · | A+B = | de Morgan's theorem
OR Operation | AND Operation | Theorem
A + A = A | A · A = A | Idempotent Law
A + 1 = 1 | A · 0 = 0 | Annulment Law
A + (A · B) = A | A · ( A + B) = A | Absorption law
 |  | Redundancy Law
 | A · (B + C) = (A · B) + (A · C) | Consensus Law
 |  | de Morgan's theorem

## Slide 39: Using a Truth Table to Prove a Boolean Expression
Example 1: Prove the associative law for the OR operation , which states that
(A + B) + C = A + (B + C)
Example 2: Use truth tables to prove the following operations
A(BC) = (AB)C = ABC
A(B + C) = AB + AC
Example 3: Prepare a truth table for the logic expression
D = AB + C

## Slide 40: MCQ 1
The expression for Absorption law is given by _________
a) A + AB = A
b) A + AB = B
c) AB + AA’ = A
d) A + B = B + A
A

## Slide 41: MCQ 2
According to Boolean law: A + 1 = ?
a) 1
b) A
c) 0
d) A’
A

## Slide 42: MCQ 3
A(A + B) = ?
a) AB
b) 1
c) (1 + AB)
d) A
D

## Slide 43: MCQ 4
DeMorgan’s theorem states that _________
a) (AB)’ = A’ + B’
b) (A + B)’ = A’ * B
c) A’ + B’ = A’B’
d) (AB)’ = A’ + B
A

## Slide 44: MCQ 5
The boolean function A + BC is a reduced form of ____________
a) AB + BC
b) (A + B)(A + C)
c) A’B + AB’C
d) (A + C)B
B

## Slide 45: MCQ 6
How many truth table entries are necessary for a four-input circuit?
a) 4
b) 8
c) 12
d) 16
D

## Slide 46: MCQ 7
Which input values will cause an AND logic gate to produce a HIGH output?
a) At least one input is HIGH
b) At least one input is LOW
c) All inputs are HIGH
d) All inputs are LOW
C

## Slide 47: MCQ 8
The basic logic gate whose output is the complement of the input is the ___________
a) OR gate
b) AND gate
c) INVERTER gate
d) XOR gate
C

## Slide 48: MCQ 9
In Boolean algebra, the OR operation is performed by which properties?
a) Associative properties
b) Commutative properties
c) Distributive properties
d) All of the Mentioned
D

## Slide 49: MCQ 10
In which of the following gates the output is 1 if and only if at least one input is 1?
a) AND
b) NOR
c) NAND
d) OR
D

## Slide 50: 4. Half adder & full adder

## Slide 51: Half adder & full adder Circuits
An Adder is a device that can add two binary digits.
It is a type of digital circuit that performs the operation of additions of two number.
It is mainly designed for the addition of binary number, but they can be used in various other applications like binary code decimal, address decoding, table index calculation, etc.
There are two types of Adder.
One is Half Adder, and another one is known as Full Adder.

## Slide 52: Half adder
There are two inputs and two outputs in a Half Adder.
Inputs are named as A and B, and the outputs are named as Sum (S) and Carry (C).
The Sum is X-OR of the input A and B. Carry is AND of the input A and B.
With the help of half adder, one can design a circuit that is capable of performing simple addition with the help of logic gates.
Let us first take a look at the addition of single bits.
0 + 0 = 0
0 + 1 = 1
1 + 0 = 1
1 + 1 = 10

## Slide 53: Half adder
These are the least possible single bit combinations.
But the result for 1 + 1 =10.
This problem can be solved with the help of an XOR gate.
The sum results can be re-written as a 2-bit output.
Thus, the above combination can be written as
0 + 0 = 00
0 + 1 = 01
1 + 0 = 01
1 + 1 = 10
Here the output “1” of “10” becomes the carry-out. SUM is the normal output and the CARRY is the carry-out.

## Slide 54: Half adder
The truth table of the half adder is as follows:
The main disadvantage of this circuit is that it can only add two inputs and if there is any carry it is neglected. Thus, the process is incomplete. To overcome this difficulty Full Adder is designed.
Inputs |  | Outputs | 
A | B | Sum (A⊕B) | Carry (AB)
0 | 0 | 0 | 0
0 | 1 | 1 | 0
1 | 0 | 1 | 0
1 | 1 | 0 | 1

## Slide 55: Full adder
The main difference between a half adder and a full adder is that the full adder has three inputs and two outputs.
The two inputs are A and B, and the third input is a carry input .
The output carry is designated as , and the normal output is designated as S.
Inputs |  |  | Outputs | 
A | B | C | COUT (AB+BC+CA) | S (A⊕B⊕C)
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 1
0 | 1 | 0 | 0 | 1
0 | 1 | 1 | 1 | 0
1 | 0 | 0 | 0 | 1
1 | 0 | 1 | 1 | 0
1 | 1 | 0 | 1 | 0
1 | 1 | 1 | 1 | 1

## Slide 56: Full adder circuit
Thus, a full adder circuit can be implemented with the help of two half adder circuits.
The first half adder circuit will be used to add A and B to produce a partial sum.
The second half adder logic can be used to add CIN to the sum produced by the first half adder circuit.
Finally, the output S is obtained.

## Slide 57: Quiz
Total number of inputs in a half adder is __________
a) 2
b) 3
c) 4
d) 1

## Slide 58: Quiz
If A and B are the inputs of a half adder, the sum is given by __________
a) A AND B
b) A OR B
c) A XOR B
d) A EX-NOR B

## Slide 59: Quiz
If A and B are the inputs of a half adder, the carry is given by __________
a) A AND B
b) A OR B
c) A XOR B
d) A EX-NOR B

## Slide 60: Quiz
The difference between half adder and full adder is __________
a) Half adder has two inputs while full adder has four inputs
b) Half adder has one output while full adder has two outputs
c) Half adder has two inputs while full adder has three inputs
d) All of the Mentioned

## Slide 61: Quiz
If A, B and C are the inputs of a full adder then the sum is given by __________
a) A AND B AND C
b) A OR B AND C
c) A XOR B XOR C
d) A OR B OR C

## Slide 62: Quiz
If A, B and C are the inputs of a full adder then the carry is given by __________
a) A AND B OR (A OR B) AND C
b) A OR B OR (A AND B) C
c) (A AND B) OR (A AND B)C
d) A XOR B XOR (A XOR B) AND C

## Slide 63: Quiz
How many AND, OR and XOR gates are required for the configuration of full adder?
a) 1, 2, 2
b) 2, 1, 2
c) 3, 1, 2
d) 4, 0, 1

## Slide 64: 5. Multiplexer & demultiplexer

## Slide 65: Multiplexer & demultiplexer
A multiplexer is a circuit that accept many input but give only one output.
A demultiplexer function exactly in the reverse of a multiplexer, that is a demultiplexer accepts only one input and gives many outputs.
Generally multiplexer and demultiplexer are used together, because of the communication systems are bi directional.

## Slide 66: Multiplexer
Multiplexer means many into one.
A multiplexer is a circuit used to select and route any one of the several input signals to a signal output.
An simple example of an non electronic circuit of a multiplexer is a single pole multi-position switch.
Multi-position switches are widely used in many electronics circuits.
However circuits that operate at high speed require the multiplexer to be automatically selected.
A mechanical switch cannot perform this task satisfactorily.
Therefore, multiplexer used to perform high speed switching are constructed of electronic components.

## Slide 67: Multiplexer
Multiplexer handle two type of data that is analog and digital.
For analog application, multiplexer are built of relays and transistor switches.
For digital application, they are built from standard logic gates.
The multiplexer used for digital applications, also called digital multiplexer, is a circuit with many input but only one output.
Data selector (:1 MUX).
Inputs: data inputs, n select lines.
Output: 1 data output line
Few types of multiplexer are 2-to-1, 4-to-1, 8-to-1, 16-to-1 multiplexer.

## Slide 68: multiplexer
Rotary Switch

## Slide 69: 2:1 Mux

## Slide 70: 4-to-1 Mux
The 4-to-1 multiplexer has 4 input bit, 2 control bits, and 1 output bit.
The four input bits are D0,D1,D2 and D3. only one of this is transmitted to the output y.
The output depends on the value of AB which is the control input.
The control input determines which of the input data bit is transmitted to the output.
For instance, as shown in fig. when AB = 00, the upper AND gate is enabled while all other AND gates are disabled. Therefore, data bit D0 is transmitted to the output, giving Y = Do.
A | B | Y
0 | 0 | D0
0 | 1 | D1
1 | 0 | D2
1 | 1 | D3

## Slide 71: Demultiplexer
Demultiplexer means one to many.
A demultiplexer is a circuit with one input and many output.
By applying control signal, we can steer any input to the output.
Few types of demultiplexer are 1-to 2, 1-to-4, 1-to-8 and 1-to 16 demultiplexer.

## Slide 72: 1-to-2 Demultiplexer
A 1-to-2 demultiplexer consists of one input line, two output lines and one select line.
The signal on the select line helps to switch the input to one of the two outputs.

## Slide 73: 1-to-4 Demultiplexer
The 1-to-4 demultiplexer has 1 input bit, 2 control bit, and 4 output bits.

## Slide 74: Mcq 1
What is a multiplexer ?
a) It is a type of decoder which decodes several inputs and gives one output
b) A multiplexer is a device which converts many signals into one
c) It takes one input and results into many output
d) It is a type of encoder which decodes several inputs and gives one output
B

## Slide 75: Mcq 2
Which combinational circuit is renowned for selecting a single input from multiple inputs & directing the binary information to output line?
a) Data Selector
b) Data distributor
c) Both data selector and data distributor
d) DeMultiplexer
A

## Slide 76: MCQ 3
In a multiplexer, the selection of a particular input line is controlled by ___________
a) Data controller
b) Selected lines
c) Logic gates
d) Both data controller and selected lines
B

## Slide 77: MCQ 4
If the number of n selected input lines is equal to 2^m then it requires _____ select lines.
a) 2
b) m
c) n
d) 2^n
B

## Slide 78: MCQ 5
How many select lines would be required for an 8-line-to-1-line multiplexer?
a) 2
b) 4
c) 8
d) 3
2^n input lines, n control lines and 1 output line available for MUX. Here, 8 input lines mean 2^3 inputs. So, 3 control lines are possible. Depending on the status of the select lines, the input is selected and fed to the output.
D

## Slide 79: MCQ 6
A basic multiplexer principle can be demonstrated through the use of a ___________
a) Single-pole relay
b) DPDT switch
c) Rotary switch
d) Linear stepper
C

## Slide 80: MCQ 7
How many NOT gates are required for the construction of a 4-to-1 multiplexer?
a) 3
b) 4
c) 2
d) 5
C

## Slide 81: MCQ 8
In the given 4-to-1 multiplexer, if c1 = 0 and c0 = 1 then the output M is ___________
a) X0
b) X1
c) X2
d) X3
B

## Slide 82: MCQ 9
4 to 1 MUX would have ____________
a) 2 inputs
b) 3 inputs
c) 4 inputs
d) 5 inputs
C

## Slide 83: MCQ 10
The two input MUX would have ____________
a) 1 select line
b) 2 select lines
c) 4 select lines
d) 3 select lines
The two input multiplexer would have n select lines in 2^n.
Thus n =1.
Therefore, it has 1 select line.
A

## Slide 84: MCQ 11
A combinational circuit that selects one from many inputs are ____________
a) Encoder
b) Decoder
c) Demultiplexer
d) Multiplexer
D

## Slide 85: MCQ 12
4 to 1 MUX would have ____________
a) 1 output
b) 2 outputs
c) 3 outputs
d) 4 outputs
A

## Slide 86: Mcq 13
The word demultiplex means ___________
a) One into many
b) Many into one
c) Distributor
d) One into many as well as Distributor
D

## Slide 87: Mcq 14
Why is a demultiplexer called a data distributor?
a) The input will be distributed to one of the outputs
b) One of the inputs will be selected for the output
c) The output will be distributed to one of the inputs
d) Single input to Single Output
A

## Slide 88: Mcq 15
In 1-to-4 demultiplexer, how many select lines are required?
a) 2
b) 3
c) 4
d) 5
A
The formula for total no. of outputs is given by 2^n, where n is the no. of select lines. Therefore, for 1:4 demultiplexer, 2 select lines are required.

## Slide 89: Mcq 16
In 1-to-4 multiplexer, if C1 = 0 & C2 = 1, then the output will be ___________
a) Y0
b) Y1
c) Y2
d) Y3
B

## Slide 90: Mcq 17
In 1-to-4 multiplexer, if C1 = 1 & C2 = 1, then the output will be ___________
a) Y0
b) Y1
c) Y2
d) Y3
D

## Slide 91: Mcq 18
How many select lines are required for a 1-to-8 demultiplexer?
a) 2
b) 3
c) 4
d) 5
B

## Slide 92: Mcq 19
How many AND gates are required for a 1-to-4 multiplexer?
a) 2
b) 6
c) 4
d) 5
C

## Slide 93: MCQ 20
In 1-to-4 multiplexer, if C1 = 1 & C2 = 1, then the output will be ____________
a) Y0
b) Y1
c) Y2
d) Y3
D

## Slide 94: 6. flipflops

## Slide 95: Flipflop
A flip-flop has two stable operating states; therefore, it can store one bit of information.
Many useful versions of flip-flops exist, differing in the manner that the clock signal and other input signals control the state of the flip-flop.
A simple flip-flop can be constructed by using two inverters, with the output of one connected to the input of the other, as shown in Figure
Two stable states are possible in the circuit.
First, the output Q of the top inverter can be high and then the output of the bottom inverter is low.
Thus, the output of the bottom inverter is labelled as .

## Slide 96: SR Flip-Flop
The simple two-inverter circuit of Figure is not very useful because no provision exists for controlling its state.
A more useful circuit is the set-reset (SR) flip-flop, consisting of two NOR gates, as shown in Figure.

## Slide 97: SR Flipflop
As long as the S and R inputs are low, the NOR gates act as inverters for the other input signal. Thus, with S and R both low, the SR flip-flop behaves just as the two-inverter circuit (simple Flipflop).
If S is high and R is low, is forced low and Q is high.
  When S returns low, the flip-flop remains in the set state (i.e., Q stays high).
On the other hand, if R becomes high and S low, Q is forced low.
  When R returns low, the flip-flop remains in the reset state (i.e., Q stays low).
In normal operation, R and S are not allowed to be high at the same time.
Thus, with R and S low, the SR flip-flop remembers which input (R or S) was high most recently.

## Slide 98: Example 1
The waveforms present at the input terminals of an SR flip-flop are shown in Figure

## Slide 99: Edge-Triggered Flip-Flops
The edge-triggered circuits respond to their inputs only at a transition in the clock signal.
At the clock transition, the flip-flop responds to the inputs present just prior to the transition.
If the clock signal is steady, either high or low, the inputs are disabled.
At the clock transition, the flip-flop responds to the inputs present just prior to the transition.
Positive-edge-triggered circuits respond when the clock signal switches from low to high.
Negative-edge-triggered circuits respond on the transition from high to low.
The positive-going edge of the clock is also called the leading edge, and the negative-going edge is called the trailing edge.

## Slide 100: D flip-flop
An example of an edge-triggered circuit is the D flip-flop, which is also known as the data flip-flop.
Its output takes the value of the input that was present just prior to the triggering clock transition.
Note, the symbols in the clock column of the truth table, indicating transitions of the clock signal from low to high.

## Slide 101: Example 2
The input signals to a positive-edge-triggered D flip-flop are shown in Figure. Sketch the output Q to scale versus time. (Assume that Q is low prior to t = 2.)

## Slide 102: JK (Jack-Kilby) Flip-Flop
Its operation is very similar to that of an SR flip-flop except that if both control inputs (J and K) are high, the state changes on the next negative-going clock edge.
Thus when both J and K are high, the output of the flipflop toggles on each cycle of the clock–switching from high to low on one negative going clock transition, back to high on the next negative transition, and so on.

## Slide 103: T Flip-flop
The name T flip-flop is termed from the nature of toggling operation.
The major applications of T flip-flop are counters and control circuits.
T flip flop is modified form of JK flip-flop making it to operate in toggling region.
Whenever the clock signal is LOW, the input is never going to affect the output state.
The clock has to be high for the inputs to get active.
Thus, T flip-flop is a controlled Bi-stable latch where the clock signal is the control signal.
Thus, the output has two stable states based on the inputs which have been discussed below.

## Slide 104: T flipflop
The T flip flop is the modified form of JK flip flop. The Q and Q’ represents the output states of the flip-flop.
According to the table, based on the input the output changes its state.
But, the important thing to consider is all these can occur only in the presence of the clock signal

## Slide 105: MCQ1
The truth table for an S-R flip-flop has how many VALID entries?
a) 1
b) 2
c) 3
d) 4
C

## Slide 106: MCQ2
Which of the following is correct for a gated D-type flip-flop?
a) The Q output is either SET or RESET as soon as the D input goes HIGH or LOW
b) The output complement follows the input when enabled
c) Only one of the inputs can be HIGH at a time
d) The output toggles if one of the inputs is held HIGH
A

## Slide 107: MCQ3
A basic S-R flip-flop can be constructed by cross-coupling of which basic logic gates?
a) AND
b) XOR
c) NOR
d) OR
C

## Slide 108: MCQ4
A basic S-R flip-flop can be constructed by cross-coupling of which basic logic gates?
a) AND
b) XOR
c) NOR
d) OR
C

## Slide 109: MCQ5
In S-R flip-flop, if Q = 0 the output is said to be ___________
a) Set
b) Reset
c) Previous state
d) Current state
B

## Slide 110: MCQ6
How many types of flip-flops are?
a) 2
b) 3
c) 4
d) 5
C

## Slide 111: MCQ7
What is one disadvantage of an S-R flip-flop?
a) It has no Enable input
b) It has a RACE condition
c) It has no clock input
d) Invalid State
D

## Slide 112: MCQ8
The characteristic of J-K flip-flop is similar to _____________
a) S-R flip-flop
b) D flip-flop
c) T flip-flop
d) Gated T flip-flop
A

## Slide 113: MCQ9
A J-K flip-flop can be obtained from the clocked S-R flip-flop by augmenting ___________
a) Two AND gates
b) Two NAND gates
c) Two NOT gates
d) Two OR gates
A

## Slide 114: MCQ10
How is a J-K flip-flop made to toggle?
a) J = 0, K = 0
b) J = 1, K = 0
c) J = 0, K = 1
d) J = 1, K = 1
D

## Slide 115: MCQ11
In J-K flip-flop, “no change” condition appears when ___________
a) J = 1, K = 1
b) J = 1, K = 0
c) J = 0, K = 1
d) J = 0, K = 0
D

## Slide 116: MCQ12
On a J-K flip-flop, when is the flip-flop in a hold condition?
a) J = 0, K = 0
b) J = 1, K = 0
c) J = 0, K = 1
d) J = 1, K = 1
A

## Slide 117: MCQ 13
The D flip-flop has _______ input.
a) 1
b) 2
c) 3
d) 4
A

## Slide 118: MCQ 14
The D flip-flop has ______ output/outputs.
a) 2
b) 3
c) 4
d) 1
A

## Slide 119: MCQ 15
In D flip-flop, D stands for _____________
a) Distant
b) Data
c) Desired
d) Delay
B

## Slide 120: MCQ 16
In D flip-flop, if clock input is LOW, the D input ___________
a) Has no effect
b) Goes high
c) Goes low
d) Has effect
A

## Slide 121: MCQ 17
In a J-K flip-flop, if J=K or K=J the resulting flip-flop is referred to as _____________
a) D flip-flop
b) S-R flip-flop
c) T flip-flop
d) S-K flip-flop
C

## Slide 122: MCQ 18
The flip-flop is only activated by _____________
a) Positive edge trigger
b) Negative edge trigger
c) Either positive or Negative edge trigger
d) Sinusoidal trigger
C

## Slide 123: MCQ 19
The flip-flops which has not having any invalid states are _____________
a) S-R, J-K, D
b) S-R, J-K, T
c) J-K, D, S-R
d) J-K, D, T
D

## Slide 124: MCQ 20
For realisation of JK flip-flop from SR flip-flop, the input J and K will be given as ___________
a) External inputs to S and R
b) Internal inputs to S and R
c) External inputs to combinational circuit
d) Internal inputs to combinational circuit
A

## Slide 125: 7. Computer organization & Memory types

## Slide 126: Computer Organization
A stored program computer has the following basic units:
  Processor - center for manipulation and control
  Memory - storage for instructions and data for currently executing programs
  I/O system - controller which communicate with "external" devices: secondary memory, display devices, networks
  Data-path & control - collection of parallel wires, transmits data, instructions, or control signal
Computer organization defines the ways in which these components are interconnected and controlled.

## Slide 127: Arithmetic and logic Unit (ALU)
ALU is responsible to perform the operation in the computer.
ALU is having collection of two types of operations:
  Arithmetic operations
  Logical operations
Consider an ALU having 4 arithmetic operations and 4 logical operation.
Consider an ALU is having four arithmetic operations. Addition, subtraction, multiplication and division. Also consider that the ALU is having four logical operations: OR, AND, NOT & EX-OR.

## Slide 128: Arithmetic and logic Unit (ALU)
To identify any one of these four logical operations or four arithmetic operations, two control lines are needed.
Also to identify the any one of these two groups- arithmetic or logical, another control line is needed.
So, with the help of three control lines, any one of these eight operations can be identified.
Control line C2 is used to identify the group: logical or arithmetic, i.e.,: arithmetic operation : logical operation.
Control lines C0 and C1 are used to identify any one of the four operations in a group. One possible combination is given here.

## Slide 129: Block Diagram of the ALU
A decode is used to decode the instruction.
The ALU has got two input registers named as A and B and one output storage register, named as C.
The input data are stored in A and B, and according to the operation specified in the control lines, the ALU perform the operation and put the result in register C.

## Slide 130: Control unit
The control unit supervises the operation of the computer, such as determining the location of the next instruction to be retrieved from memory and setting up the ALU to carry out operations on data.

## Slide 131: Programs
Programs are sequences of instructions stored in memory.
Typically, the controller fetches (i.e., retrieves) an instruction, determines what operation is called for by the instruction, fetches data from memory as required, causes the ALU to perform the operation, and writes results back to memory.
Then, the next instruction is fetched, and the process is repeated.

## Slide 132: Buses
The various elements of a computer are connected by buses, which are sets of conductors that transfer multiple bits at a time.
For example, the data bus transfers data (and instructions) between the CPU and memory (or I/O devices).
The control buses are used to direct the operations of the computer.
Buses can be bidirectional. In other words, they can transfer data in either direction.

## Slide 133: Input - Output
Some examples of I/O devices are keyboards, display devices, and printers.
Input Devices
Output Devices
Both

## Slide 134: Memory types
Several types of memory are used in computers:
Read-and-write memory (RAM),
Read-only memory (ROM), and
Mass storage.

## Slide 135: RAM
Read-and-write memory (RAM) is used for storing data, instructions, and results during execution of a program.
Usually, the information that is stored in RAM is lost when power is removed. Thus, we say that RAM is volatile.
Originally, the acronym RAM meant random access memory, but the term has changed its meaning over time.
There are two types of RAM in common use.
  Static RAM and
  Dynamic RAM

## Slide 136: Static and dynamic ram
In static RAM, the storage cells are SR flip-flops that can store data indefinitely, provided that power is applied continuously.
In dynamic RAM, information is stored in each cell as charge (or lack of charge) on a capacitor.
Because the charge leaks off the capacitors, it is necessary to refresh the information periodically.
This makes the use of dynamic RAM more complex than the use of static RAM.
The advantage of dynamic RAM is that the basic storage cell is smaller, so that chips with larger capacities are available.
A relatively small amount of RAM is needed in most control applications, and it is simpler to use static RAM.

## Slide 137: ROM
In normal operation, read-only memory (ROM) can be read, but not written to.
The chief advantages of ROM are that data can be read quickly in random order and that information is not lost when power is turned off.
Thus, we say that ROM is nonvolatile (i.e., permanent).
ROM is useful for storing programs such as the boot program, which is executed automatically when power is applied to a computer.
Several types of ROM exist.
  mask-programmable ROM,
  programmable read-only memory (PROM)
  Erasable PROM (EPROM)
  Electrically erasable PROMs (EEPROMs)
  Flash memory

## Slide 138: ROM
In mask-programmable ROM, the data are written when the chip is manufactured.
In programmable read-only memory (PROM), data can be written by special circuits that blow tiny fuses or leave them unblown, depending on whether the data bits are zeros or ones.
Erasable PROM (EPROM) is another type that can be erased by exposure to ultraviolet light (through a window in the chip package) and rewritten by using special circuits.
Electrically erasable PROMs (EEPROMs) can be erased by applying proper voltages to the chip.
Flash memory is a nonvolatile technology in which data can be erased and rewritten relatively quickly in blocks of locations, ranging in size from 512 bytes up to 512 Kbytes.

## Slide 139: Mass Storage
Mass-storage units include hard disks and flash memory, both of which are read/write memory.
Another type is CD-ROM (Compact Disk-Read Only Memory) and DVD-ROM (Digital Versatile Disc-Read Only Memory) disks, which are used for storing large amounts of data.
Mass storage is the least expensive type of memory per unit of capacity

## Slide 140: MCQ 1
The instruction used in a program for executing them is stored in the __________
a) CPU
b) Control Unit
c) Memory
d) Microprocessor
C

## Slide 141: MCQ 2
CD-ROM refers to __________
a) Floppy disk
b) Compact Disk-Read Only Memory
c) Compressed Disk-Read Only Memory
d) Compressed Disk- Random Access Memory
B

## Slide 142: MCQ 3
A ROM is defined as __________
a) Read Out Memory
b) Read Once Memory
c) Read Only Memory
d) Read One Memory
C

## Slide 143: MCQ 4
The full form of PROM is __________
a) Previous Read Only Memory
b) Programmable Read Out Memory
c) Programmable Read Only Memory
d) Previous Read Out Memory
C

## Slide 144: MCQ 5
The full form of EPROM is __________
a) Easy Programmable Read Only Memory
b) Erasable Programmable Read Only Memory
c) Eradicate Programmable Read Only Memory
d) Easy Programmable Read Out Memory
B

## Slide 145: MCQ 6
The full form of EPROM is __________
a) Easy Programmable Read Only Memory
b) Erasable Programmable Read Only Memory
c) Eradicate Programmable Read Only Memory
d) Easy Programmable Read Out Memory
B

## Slide 146: MCQ 7
A memory is a collection of ____________
a) Unit cells
b) Storage cells
c) Data cells
d) Binary cells
B

## Slide 147: MCQ 8
Mask programming is also known as __________
a) EPROM
b) PROM
c) Custom programming
d) Both PROM and EPROM
C

## Slide 148: MCQ 9
These devices provide a means of communication between a computer and outer world.
a) I/O
b) Storage
c) Compact
d) Drivers
A

## Slide 149: MCQ 10
Identify the blank space in the diagram.
a) Processor
b) Memory
c) CPU
d) Storage
A

## Slide 150: MCQ 11
Which of the following is not a point-and-draw device?
a) Keypad
b) Trackball
c) Touch screen
d) Mouse
A

## Slide 151: MCQ 12
The ALU gives the output of the operations and the output is stored in the ________
a) Memory Devices
b) Registers
c) Flags
d) Output Unit
B

## Slide 152: 8. counters

## Slide 153: Counters
A Counter is a device which stores (and sometimes displays) the number of times a particular event or process has occurred, often in relationship to a clock signal.
Counters are used in digital electronics for counting purpose, they can count specific event happening in the circuit.
Counters are broadly divided into two categories
  Asynchronous counter
  Synchronous counter

## Slide 154: Asynchronous Counter
In asynchronous counter we don’t use universal clock, only first flip flop is driven by main clock and the clock input of rest of the following flip flop is driven by output of previous flip flops.
It is evident from timing diagram that Q0 is changing as soon as the rising edge of clock pulse is encountered, Q1 is changing when rising edge of Q0 is encountered (because Q0 is like clock pulse for second flip flop) and so on. In this way ripples are generated through Q0,Q1,Q2,Q3 hence it is also called RIPPLE counter.

## Slide 155: Synchronous Counter
Unlike the asynchronous counter, synchronous counter has one global clock which drives each flip flop so output changes in parallel.
The one advantage of synchronous counter over asynchronous counter is, it can operate on higher frequency than asynchronous counter as it does not have cumulative delay because of same clock is given to each flip flop.

## Slide 156: Synchronous Counter
From circuit diagram we see that Q0 bit gives response to each falling edge of clock while Q1 is dependent on Q0, Q2 is dependent on Q1 and Q0, Q3 is dependent on Q2, Q1 and Q0.

## Slide 157: MCQ 1
1. In digital logic, a counter is a device which ____________
a) Counts the number of outputs
b) Stores the number of times a particular event or process has occurred
c) Stores the number of times a clock pulse rises and falls
d) Counts the number of inputs
B

## Slide 158: MCQ 2
A counter circuit is usually constructed of ____________
a) A number of latches connected in cascade form
b) A number of NAND gates connected in cascade form
c) A number of flip-flops connected in cascade
d) A number of NOR gates connected in cascade form
C

## Slide 159: MCQ 3
Ripple counters are also called ____________
a) SSI counters
b) Asynchronous counters
c) Synchronous counters
d) VLSI counters
B

## Slide 160: MCQ 4
One of the major drawbacks to the use of asynchronous counters is that ____________
a) Low-frequency applications are limited because of internal propagation delays
b) High-frequency applications are limited because of internal propagation delays
c) Asynchronous counters do not have major drawbacks and are suitable for use in high- and low-frequency counting applications
d) Asynchronous counters do not have propagation delays, which limits their use in high-frequency applications
B

## Slide 161: MCQ 5
Internal propagation delay of asynchronous counter is removed by ____________
a) Ripple counter
b) Ring counter
c) Modulus counter
d) Synchronous counter
D