## Slide 1: Module 3: Digital Systems

## Slide 2: 2. Logic gates

## Slide 3: logic gates – Symbols & Truth Table
In this section, we consider circuits called logic gates that combine several logic variable inputs to produce a logic-variable output.
AND Gate
NOT Gate
OR Gate
NAND Gate
NOR Gate
XOR Gate

## Slide 4: AND Gate
The AND operation on two logic variables, A and B, is represented as AB, read as “A and B.”
The AND operation is also called logical multiplication.

## Slide 5: Three input and gate

## Slide 6: Not gate
The NOT operation on a logic variable is represented by placing a bar over the symbol for the logic variable. The symbol is read as “not A” or as “A inverse.” If A is 0, is 1, and vice versa.

## Slide 7: Or gate
The OR operation of logic variables is written as A+B, which is read as “A or B.”
Notice that A+B is 1 if A or B (or both) are 1.
The OR operation is also called logical addition.

## Slide 8: Three-input OR gate

## Slide 9: Nand gate
The NAND gate is equivalent to an AND gate followed by an inverter.
Notice that the symbol is the same as for an AND gate, with a bubble at the output terminal to indicate that the output has been inverted after the AND operation.
A | B | AND (AB) | NAND ()
0 | 0 | 0 | 1
0 | 1 | 0 | 1
1 | 0 | 0 | 1
1 | 1 | 1 | 0
A | B | AND (AB) | 
0 | 0 | 0 | 1
0 | 1 | 0 | 1
1 | 0 | 0 | 1
1 | 1 | 1 | 0

## Slide 10: Nor gate
Similarly, the NOR gate is equivalent to an OR gate followed by an inverter.
A | B | OR (A+B) | NOR ()
0 | 0 | 0 | 1
0 | 1 | 1 | 0
1 | 0 | 1 | 0
1 | 1 | 1 | 0
A | B | OR (A+B) | 
0 | 0 | 0 | 1
0 | 1 | 1 | 0
1 | 0 | 1 | 0
1 | 1 | 1 | 0

## Slide 11: Xor gate
The exclusive-OR (XOR) operation for two logic variables A and B is represented by A ⊕ B and is defined by
0 ⊕ 0 = 0
1 ⊕ 0 = 1
0 ⊕ 1 = 1
1 ⊕ 1 = 0
Notice that the XOR operation yields 1 if A is 1 or if B is 1, but yields 0 if both A and B are 1. The XOR operation is also known as modulo-two addition.
A | B | XOR
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
A⊕B = A+B

## Slide 12: Logic IC’s

## Slide 13: Example 1
Write a Boolean expression for the output of the logic circuit

## Slide 14: Example 2
Write a Boolean expression for the output of the logic circuit

## Slide 15: Example 3
Write a Boolean expression for the output of the logic circuit

## Slide 16: Example 4
Write a Boolean expression for the output of the logic circuit

## Slide 17: Example 5
Write a Boolean expression for the output of the logic circuit
Also give the truth table for the circuit

## Slide 18: Example 6
Write a Boolean expression for the output of the logic circuit
Also give the truth table for the circuit

## Slide 19: 3. Boolean Algebra
Postulates and Theorems

## Slide 20: Postulates
Assume A, B, and C are logical states that can have the values 0 (false) and 1 (true).
"+" means OR, "·" means AND, and [] means NOT A.
OR Operation | AND Operation | Law
A + 0 = A | A · 1 = A | Identity
A + = 1 | A · = 0 | Complement
A + B = B + A | A · B = B · A | Commutative Law
A + (B + C) = (A + B) + C | A · (B · C) = (A · B) · C | Associative Law
A + (B · C) = (A + B) · (A + C) | A · (B + C) = (A · B) + (A · C) | Distributive Law
OR Operation | AND Operation | Law
A + 0 = A | A · 1 = A | Identity
 |  | Complement
A + B = B + A | A · B = B · A | Commutative Law
A + (B + C) = (A + B) + C | A · (B · C) = (A · B) · C | Associative Law
A + (B · C) = (A + B) · (A + C) | A · (B + C) = (A · B) + (A · C) | Distributive Law

## Slide 21: Theorems
OR Operation | AND Operation | Theorem
A + A = A | A · A = A | Idempotent Law
A + 1 = 1 | A · 0 = 0 | Annulment Law
A + (A · B) = A | A · ( A + B) = A | Absorption law
A + ( · B) = A + B | A · ( + B) = A · B | Redundancy Law
(A · B) + ( · C) + (B · C) = (A · B) + ( · C) | A · (B + C) = (A · B) + (A · C) | Consensus Law
= · | A+B = | de Morgan's theorem
OR Operation | AND Operation | Theorem
A + A = A | A · A = A | Idempotent Law
A + 1 = 1 | A · 0 = 0 | Annulment Law
A + (A · B) = A | A · ( A + B) = A | Absorption law
 |  | Redundancy Law
 | A · (B + C) = (A · B) + (A · C) | Consensus Law
 |  | de Morgan's theorem

## Slide 22: Using a Truth Table to Prove a Boolean Expression
Example 1: Prove the associative law for the OR operation , which states that
(A + B) + C = A + (B + C)
Example 2: Use truth tables to prove the following operations
A(BC) = (AB)C = ABC
A(B + C) = AB + AC
Example 3: Prepare a truth table for the logic expression
D = AB + C

## Slide 23: MCQ 1
The expression for Absorption law is given by _________
a) A + AB = A
b) A + AB = B
c) AB + AA’ = A
d) A + B = B + A
A

## Slide 24: MCQ 2
According to Boolean law: A + 1 = ?
a) 1
b) A
c) 0
d) A’
A

## Slide 25: MCQ 3
A(A + B) = ?
a) AB
b) 1
c) (1 + AB)
d) A
D

## Slide 26: MCQ 4
DeMorgan’s theorem states that _________
a) (AB)’ = A’ + B’
b) (A + B)’ = A’ * B
c) A’ + B’ = A’B’
d) (AB)’ = A’ + B
A

## Slide 27: MCQ 5
The boolean function A + BC is a reduced form of ____________
a) AB + BC
b) (A + B)(A + C)
c) A’B + AB’C
d) (A + C)B
B

## Slide 28: MCQ 6
How many truth table entries are necessary for a four-input circuit?
a) 4
b) 8
c) 12
d) 16
D

## Slide 29: MCQ 7
Which input values will cause an AND logic gate to produce a HIGH output?
a) At least one input is HIGH
b) At least one input is LOW
c) All inputs are HIGH
d) All inputs are LOW
C

## Slide 30: MCQ 8
The basic logic gate whose output is the complement of the input is the ___________
a) OR gate
b) AND gate
c) INVERTER gate
d) XOR gate
C

## Slide 31: MCQ 9
In Boolean algebra, the OR operation is performed by which properties?
a) Associative properties
b) Commutative properties
c) Distributive properties
d) All of the Mentioned
D

## Slide 32: MCQ 10
In which of the following gates the output is 1 if and only if at least one input is 1?
a) AND
b) NOR
c) NAND
d) OR
D