## Slide 1: Module 3: Digital Systems

## Slide 2: 4. Half adder & full adder

## Slide 3: Half adder & full adder Circuits
An Adder is a device that can add two binary digits.
It is a type of digital circuit that performs the operation of additions of two number.
It is mainly designed for the addition of binary number, but they can be used in various other applications like binary code decimal, address decoding, table index calculation, etc.
There are two types of Adder.
One is Half Adder, and another one is known as Full Adder.

## Slide 4: Half adder
There are two inputs and two outputs in a Half Adder.
Inputs are named as A and B, and the outputs are named as Sum (S) and Carry (C).
The Sum is X-OR of the input A and B. Carry is AND of the input A and B.
With the help of half adder, one can design a circuit that is capable of performing simple addition with the help of logic gates.
Let us first take a look at the addition of single bits.
0 + 0 = 0
0 + 1 = 1
1 + 0 = 1
1 + 1 = 10

## Slide 5: Half adder
These are the least possible single bit combinations.
But the result for 1 + 1 =10.
This problem can be solved with the help of an XOR gate.
The sum results can be re-written as a 2-bit output.
Thus, the above combination can be written as
0 + 0 = 00
0 + 1 = 01
1 + 0 = 01
1 + 1 = 10
Here the output “1” of “10” becomes the carry-out. SUM is the normal output and the CARRY is the carry-out.

## Slide 6: Half adder
The truth table of the half adder is as follows:
The main disadvantage of this circuit is that it can only add two inputs and if there is any carry it is neglected. Thus, the process is incomplete. To overcome this difficulty Full Adder is designed.
Inputs |  | Outputs | 
A | B | Sum (A⊕B) | Carry (AB)
0 | 0 | 0 | 0
0 | 1 | 1 | 0
1 | 0 | 1 | 0
1 | 1 | 0 | 1

## Slide 7: Full adder
The main difference between a half adder and a full adder is that the full adder has three inputs and two outputs.
The two inputs are A and B, and the third input is a carry input .
The output carry is designated as , and the normal output is designated as S.
Inputs |  |  | Outputs | 
A | B | C | COUT (AB+BC+CA) | S (A⊕B⊕C)
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 1
0 | 1 | 0 | 0 | 1
0 | 1 | 1 | 1 | 0
1 | 0 | 0 | 0 | 1
1 | 0 | 1 | 1 | 0
1 | 1 | 0 | 1 | 0
1 | 1 | 1 | 1 | 1

## Slide 8: Full adder circuit
Thus, a full adder circuit can be implemented with the help of two half adder circuits.
The first half adder circuit will be used to add A and B to produce a partial sum.
The second half adder logic can be used to add CIN to the sum produced by the first half adder circuit.
Finally, the output S is obtained.

## Slide 9: Quiz
Total number of inputs in a half adder is __________
a) 2
b) 3
c) 4
d) 1

## Slide 10: Quiz
If A and B are the inputs of a half adder, the sum is given by __________
a) A AND B
b) A OR B
c) A XOR B
d) A EX-NOR B

## Slide 11: Quiz
If A and B are the inputs of a half adder, the carry is given by __________
a) A AND B
b) A OR B
c) A XOR B
d) A EX-NOR B

## Slide 12: Quiz
The difference between half adder and full adder is __________
a) Half adder has two inputs while full adder has four inputs
b) Half adder has one output while full adder has two outputs
c) Half adder has two inputs while full adder has three inputs
d) All of the Mentioned

## Slide 13: Quiz
If A, B and C are the inputs of a full adder then the sum is given by __________
a) A AND B AND C
b) A OR B AND C
c) A XOR B XOR C
d) A OR B OR C

## Slide 14: Quiz
If A, B and C are the inputs of a full adder then the carry is given by __________
a) A AND B OR (A OR B) AND C
b) A OR B OR (A AND B) C
c) (A AND B) OR (A OR B)C
d) A XOR B XOR (A XOR B) AND C

## Slide 15: Quiz
How many AND, OR and XOR gates are required for the configuration of full adder?
a) 1, 2, 2
b) 2, 1, 2
c) 3, 1, 2
d) 4, 0, 1

## Slide 16: 5. Multiplexer & demultiplexer

## Slide 17: Multiplexer & demultiplexer
A multiplexer is a circuit that accept many input but give only one output.
A demultiplexer function exactly in the reverse of a multiplexer, that is a demultiplexer accepts only one input and gives many outputs.
Generally multiplexer and demultiplexer are used together, because of the communication systems are bi directional.

## Slide 18: Multiplexer
Multiplexer means many into one.
A multiplexer is a circuit used to select and route any one of the several input signals to a signal output.
An simple example of an non electronic circuit of a multiplexer is a single pole multi-position switch.
Multi-position switches are widely used in many electronics circuits.
However circuits that operate at high speed require the multiplexer to be automatically selected.
A mechanical switch cannot perform this task satisfactorily.
Therefore, multiplexer used to perform high speed switching are constructed of electronic components.

## Slide 19: Multiplexer
Multiplexer handle two type of data that is analog and digital.
For analog application, multiplexer are built of relays and transistor switches.
For digital application, they are built from standard logic gates.
The multiplexer used for digital applications, also called digital multiplexer, is a circuit with many input but only one output.
Data selector (:1 MUX).
Inputs: data inputs, n select lines.
Output: 1 data output line
Few types of multiplexer are 2-to-1, 4-to-1, 8-to-1, 16-to-1 multiplexer.

## Slide 20: multiplexer
Rotary Switch

## Slide 21: 2:1 Mux

## Slide 22: 4-to-1 Mux
The 4-to-1 multiplexer has 4 input bit, 2 control bits, and 1 output bit.
The four input bits are D0,D1,D2 and D3. only one of this is transmitted to the output y.
The output depends on the value of AB which is the control input.
The control input determines which of the input data bit is transmitted to the output.
For instance, as shown in fig. when AB = 00, the upper AND gate is enabled while all other AND gates are disabled. Therefore, data bit D0 is transmitted to the output, giving Y = Do.
A | B | Y
0 | 0 | D0
0 | 1 | D1
1 | 0 | D2
1 | 1 | D3

## Slide 23: Demultiplexer
Demultiplexer means one to many.
A demultiplexer is a circuit with one input and many output.
By applying control signal, we can steer any input to the output.
Few types of demultiplexer are 1-to 2, 1-to-4, 1-to-8 and 1-to 16 demultiplexer.

## Slide 24: 1-to-2 Demultiplexer
A 1-to-2 demultiplexer consists of one input line, two output lines and one select line.
The signal on the select line helps to switch the input to one of the two outputs.

## Slide 25: 1-to-4 Demultiplexer
The 1-to-4 demultiplexer has 1 input bit, 2 control bit, and 4 output bits.

## Slide 26: Mcq 1
What is a multiplexer ?
a) It is a type of decoder which decodes several inputs and gives one output
b) A multiplexer is a device which converts many signals into one
c) It takes one input and results into many output
d) It is a type of encoder which decodes several inputs and gives one output
B

## Slide 27: Mcq 2
Which combinational circuit is renowned for selecting a single input from multiple inputs & directing the binary information to output line?
a) Data Selector
b) Data distributor
c) Both data selector and data distributor
d) DeMultiplexer
A

## Slide 28: MCQ 3
In a multiplexer, the selection of a particular input line is controlled by ___________
a) Data controller
b) Selected lines
c) Logic gates
d) Both data controller and selected lines
B

## Slide 29: MCQ 4
If the number of n selected input lines is equal to 2^m then it requires _____ select lines.
a) 2
b) m
c) n
d) 2^n
B

## Slide 30: MCQ 5
How many select lines would be required for an 8-line-to-1-line multiplexer?
a) 2
b) 4
c) 8
d) 3
2^n input lines, n control lines and 1 output line available for MUX. Here, 8 input lines mean 2^3 inputs. So, 3 control lines are possible. Depending on the status of the select lines, the input is selected and fed to the output.
D

## Slide 31: MCQ 6
A basic multiplexer principle can be demonstrated through the use of a ___________
a) Single-pole relay
b) DPDT switch
c) Rotary switch
d) Linear stepper
C

## Slide 32: MCQ 7
How many NOT gates are required for the construction of a 4-to-1 multiplexer?
a) 3
b) 4
c) 2
d) 5
C

## Slide 33: MCQ 8
In the given 4-to-1 multiplexer, if c1 = 0 and c0 = 1 then the output M is ___________
a) X0
b) X1
c) X2
d) X3
B

## Slide 34: MCQ 9
4 to 1 MUX would have ____________
a) 2 inputs
b) 3 inputs
c) 4 inputs
d) 5 inputs
C

## Slide 35: MCQ 10
The two input MUX would have ____________
a) 1 select line
b) 2 select lines
c) 4 select lines
d) 3 select lines
The two input multiplexer would have n select lines in 2^n.
Thus n =1.
Therefore, it has 1 select line.
A

## Slide 36: MCQ 11
A combinational circuit that selects one from many inputs are ____________
a) Encoder
b) Decoder
c) Demultiplexer
d) Multiplexer
D

## Slide 37: MCQ 12
4 to 1 MUX would have ____________
a) 1 output
b) 2 outputs
c) 3 outputs
d) 4 outputs
A

## Slide 38: Mcq 13
The word demultiplex means ___________
a) One into many
b) Many into one
c) Distributor
d) One into many as well as Distributor
D

## Slide 39: Mcq 14
Why is a demultiplexer called a data distributor?
a) The input will be distributed to one of the outputs
b) One of the inputs will be selected for the output
c) The output will be distributed to one of the inputs
d) Single input to Single Output
A

## Slide 40: Mcq 15
In 1-to-4 demultiplexer, how many select lines are required?
a) 2
b) 3
c) 4
d) 5
A
The formula for total no. of outputs is given by 2^n, where n is the no. of select lines. Therefore, for 1:4 demultiplexer, 2 select lines are required.

## Slide 41: Mcq 16
In 1-to-4 multiplexer, if C1 = 0 & C2 = 1, then the output will be ___________
a) Y0
b) Y1
c) Y2
d) Y3
B

## Slide 42: Mcq 17
In 1-to-4 multiplexer, if C1 = 1 & C2 = 1, then the output will be ___________
a) Y0
b) Y1
c) Y2
d) Y3
D

## Slide 43: Mcq 18
How many select lines are required for a 1-to-8 demultiplexer?
a) 2
b) 3
c) 4
d) 5
B

## Slide 44: Mcq 19
How many AND gates are required for a 1-to-4 multiplexer?
a) 2
b) 6
c) 4
d) 5
C

## Slide 45: MCQ 20
In 4-to-1 multiplexer, if C1 = 1 & C2 = 1, then the output will be ____________
a) Y0
b) Y1
c) Y2
d) Y3
D