## Slide 1: The ARM Instruction Set
ARM
Advanced RISC Machines

## Slide 2: Main features of the ARM Instruction Set
All instructions are 32 bits long.
Most instructions execute in a single cycle.
Every instruction can be conditionally executed.
A load/store architecture
  Data processing instructions act only on registers
    Three operand format
    Combined ALU and shifter for high speed bit manipulation
  Specific memory access instructions with powerful auto-indexing addressing modes.
    32 bit and 8 bit data types
      and also 16 bit data types on ARM Architecture v4.
    Flexible multiple register load and store instructions
Instruction set extension via coprocessors

## Slide 3: Processor Modes
The ARM has six operating modes:
  User (unprivileged mode under which most tasks run)
  FIQ (entered when a high priority (fast) interrupt is raised)
  IRQ (entered when a low priority (normal) interrupt is raised)
  Supervisor (entered on reset and when a Software Interrupt instruction is executed)
  Abort (used to handle memory access violations)
  Undef (used to handle undefined instructions)
ARM Architecture Version 4 adds a seventh mode:
  System (privileged mode using the same registers as user mode)

## Slide 4: The Registers
The registers are arranged into several banks, with the accessible bank being governed by the processor mode. Each mode can access
  a particular set of r0-r12 registers
  a particular r13 (the stack pointer) and r14 (link register)
  r15 (the program counter)
  cpsr (the current program status register)
and privileged modes can also access
  a particular spsr (saved program status register)

## Slide 5: Register Organisation
General registers and Program Counter
Program Status Registers
r15 (pc)
r14 (lr)
r13 (sp)
r14_svc
r13_svc
r14_irq
r13_irq
r14_abt
r13_abt
r14_undef
r13_undef
User32 / System
FIQ32
Supervisor32
Abort32
IRQ32
Undefined32
cpsr
sprsr_fiq
sprsr_fiq
sprsr_fiq
spsr_abt
spsr_svc
sprsr_fiq
sprsr_fiq
spsr_fiq
sprsr_fiq
sprsr_fiq
sprsr_fiq
sprsr_fiq
sprsr_fiq
spsr_irq
r12
r10
r11
r9
r8
r7
r4
r5
r2
r1
r0
r3
r6
r7
r4
r5
r2
r1
r0
r3
r6
r12
r10
r11
r9
r8
r7
r4
r5
r2
r1
r0
r3
r6
r12
r10
r11
r9
r8
r7
r4
r5
r2
r1
r0
r3
r6
r12
r10
r11
r9
r8
r7
r4
r5
r2
r1
r0
r3
r6
r12
r10
r11
r9
r8
r7
r4
r5
r2
r1
r0
r3
r6
r15 (pc)
r15 (pc)
r15 (pc)
r15 (pc)
r15 (pc)
cpsr
cpsr
cpsr
cpsr
cpsr
r14_fiq
r13_fiq
r12_fiq
r10_fiq
r11_fiq
r9_fiq
r8_fiq
sprsr_fiq
sprsr_fiq
sprsr_fiq
sprsr_fiq
sprsr_fiq
spsr_undef

## Slide 6: Accessing Registers using ARM Instructions
No breakdown of currently accessible registers.
  All instructions can access r0-r14 directly.
  Most instructions also allow use of the PC.
Specific instructions to allow access to CPSR and SPSR.
Note : When in a privileged mode, it is also possible to load / store the (banked out) user mode registers to or from memory.
  See later for details.

## Slide 7: The Program Status Registers (CPSR and SPSRs)
Copies of the ALU status flags (latched if the
instruction has the "S" bit set).
N = Negative result from ALU flag.
Z = Zero result from ALU flag.
C = ALU operation Carried out
V = ALU operation oVerflowed
* Interrupt Disable bits.
I = 1, disables the IRQ.
F = 1, disables the FIQ.
* T Bit (Architecture v4T only)
T = 0, Processor in ARM state
T = 1, Processor in Thumb state
* Condition Code Flags
Mode
N
Z
C
V
28
31
8
4
0
I F T
* Mode Bits
M[4:0] define the processor mode.
Notes: Current Program Status Register (CPSR) can be considered as an extension of the PC. It contains the:
  condition code flags, N,Z,C,V.
  interrupt (FIQ, IRQ) disable bits
  mode bits
  T bit
    Software must never change value in TBIT. If this happens, the processor will enter an unpredictable state.
Lower 28 bits known as the "control bits".
Bits other than the specified interrupt and mode bits are reserved for future processors, and no program should depend on their values.
The condition codes in the CPSR will be preserved or updated depending on the value of the S bit in the instruction.
Some instructions do alter condition flags regardless of “S”, ie CMN, CMP, TST and TEQ (return no other result).
Mode field bigger than needs to be - just history.
Only six modes valid on pre-ARM Architecture v4 chips.
SPSRs
  Also five other PSRs, the Saved Program Status Registers, one for each privilege mode, into which a copy of the CPSR is loaded when an exception occurs.

## Slide 8: The Program Counter (R15)
When the processor is executing in ARM state:
  All instructions are 32 bits in length
  All instructions must be word aligned
  Therefore the PC value is stored in bits [31:2] with bits [1:0] equal to zero (as instruction cannot be halfword or byte aligned).
R14 is used as the subroutine link register (LR) and stores the return address when Branch with Link operations are performed, calculated from the PC.
Thus to return from a linked branch
  MOV r15,r14
or
  MOV pc,lr
Notes: PC held in register R15
  Instructions always a word long, so must be aligned with word boundaries. But addresses specified in bytes, so 2 lsbs will be zero.
  ie bits [31:2] store word address, bits [1:0] always zero.
R15 may :
  be specified as the base register (Rn) in Load and Store instructions, allowing PC-relative addressing to be used.
  be the destination register, Rd, for instructions. When the “S” bit is not set the operation overwrites R15 without affecting the CPSR. When the “S” bit is set, in a privileged mode, then SPSR_<mode> is transferred to CPSR at the same time R15 is loaded.

## Slide 9: The Instruction Pipeline
The ARM uses a pipeline in order to increase the speed of the flow of instructions to the processor.
  Allows several operations to be undertaken simultaneously, rather than serially.
Rather than pointing to the instruction being executed, the PC points to the instruction being fetched.
FETCH
DECODE
EXECUTE
Instruction fetched from memory
Decoding of registers used in instruction
Register(s) read from Register Bank
Shift and ALU operation
Write register(s) back to Register Bank
PC
PC - 4
PC - 8
ARM
Notes: Each instruction is one word (or 32 bits)
  Thus each stage in pipeline is one word
  In other words 4 bytes, hence the offsets of 4 and 8 used here.
Most instructions execute in a single cycle
  Helps to keep the pipeline operating efficiently - only stalls if executing instruction takes several cycles.
  Thus every cycle, processor can be loading one instruction, decoding another, whilst executing a third.
Typically the PC can be assumed to be current instruction plus 8
  Cases when not case include
    When exceptions taken the address stored in LR varies - see Exception Handling module for more details.
    When PC used in some data processing operations value is unpredictable - see datasheet

## Slide 10: Data processing Instructions
Largest family of ARM instructions, all sharing the same instruction format.
Contains:
  Arithmetic operations
  Comparisons (no results - just set condition codes)
  Logical operations
  Data movement between registers
Remember, this is a load / store architecture
  These instruction only work on registers, NOT memory.
They each perform a specific operation on one or two operands.
  First operand always a register - Rn
  Second operand sent to the ALU via barrel shifter.
We will examine the barrel shifter shortly.

## Slide 11: Arithmetic Operations
Operations are:
  ADD operand1 + operand2
  ADC operand1 + operand2 + carry
  SUB operand1 - operand2
  SBC operand1 - operand2 + carry -1
  RSB operand2 - operand1
  RSC operand2 - operand1 + carry - 1
Syntax:
  <Operation>{<cond>}{S} Rd, Rn, Operand2
Examples
  ADD r0, r1, r2
  SUBGT r3, r3, #1
  RSBLES r4, r5, #5

## Slide 12: Comparisons
The only effect of the comparisons is to
  UPDATE THE CONDITION FLAGS.
Operations are:
  CMP operand1 - operand2, but result not written
  CMN operand1 + operand2, but result not written
  TST operand1 AND operand2, but result not written
  TEQ operand1 EOR operand2, but result not written
Syntax:
  <Operation>{<cond>} Rn, Operand2
Examples:
  CMP r0, r1
  TSTEQ r2, #5

## Slide 13: Logical Operations
Operations are:
  AND operand1 AND operand2
  EOR operand1 EOR operand2
  ORR operand1 OR operand2
  BIC operand1 AND NOT operand2 [ie bit clear]
Syntax:
  <Operation>{<cond>}{S} Rd, Rn, Operand2
Examples:
  AND r0, r1, r2
  BICEQ r2, r3, #7
  EORS r1,r3,r0

## Slide 14: Data Movement
Operations are:
  MOV operand2
  MVN NOT operand2
Note that these make no use of operand1.
Syntax:
  <Operation>{<cond>}{S} Rd, Operand2
Examples:
  MOV r0, r1
  MOVS r2, #10
  MVNEQ r1,#0

## Slide 15: The Barrel Shifter
The ARM doesn’t have actual shift instructions.
Instead it has a barrel shifter which provides a mechanism to carry out shifts as part of other instructions.
So what operations does the barrel shifter support?

## Slide 16: Barrel Shifter - Left Shift
Shifts left by the specified amount (multiplies by powers of two) e.g.
  LSL #5 = multiply by 32
Logical Shift Left (LSL)
Destination
CF
0
Notes: Effectively x 2n.
  bits of operand shifted left by specified number of bits.
  Zeros are inserted into the right most end of the word
  last bit removed from the left most end placed in carry flag.
LSL #0 does nothing and is the default shift if none is specified.

## Slide 17: Barrel Shifter - Right Shifts
Logical Shift Right
Shifts right by the specified amount (divides by powers of two) e.g.
LSR #5 = divide by 32
Arithmetic Shift Right
Shifts right (divides by powers of two) and preserves the sign bit, for 2's complement operations. e.g.
ASR #5 = divide by 32
Destination
CF
Destination
CF
Logical Shift Right
Arithmetic Shift Right
...0
Sign bit shifted in
Notes: LSR moves each bit of the register (Rm) to the right by the specified amount.
eg / LSR #5
  all bits are moved 5 places to right (i.e. into less significant positions).
  most significant positions then filled with zeros
  least significant five bits of Rm are removed. The last of these five bits becomes the shifter Carry output, and may set the CPSR's C flag (when the ALU operation is in the logical class).
An LSR 0 is translated into an LSR 32, to put bit 31 of the word into the carry flag.
ASR similar to LSR except that
  high bits are filled with bit 31 of Rm (the sign bit) instead of zeros.
  This preserves the sign in 2's complement notation.
eg/
  Divide a 2's complement number 10000010B (or -126) in Ra by 2.
MOV Ra, Ra, ASR #2
  From Ra=10000010B we get RA=11000001B (or - 63)
An ASR #0 is translated into an ASR #32, to propagate bit 31 of the word into every bit in the word as well as the carry flag.

## Slide 18: Barrel Shifter - Rotations
Rotate Right (ROR)
• Similar to an ASR but the bits wrap around as they leave the LSB and appear as the MSB.
e.g. ROR #5
Note the last bit rotated is also used as the Carry Out.
Rotate Right Extended (RRX)
• This operation uses the CPSR C flag as a 33rd bit.
Rotates right by 1 bit. Encoded as ROR #0.
Destination
CF
Rotate Right
Destination
CF
Rotate Right through Carry
Notes: Rotate Right (ROR), and Rotate Right Extended (RRX) operations
  used to manipulate the bits in a register without destroying those bits.
  move each bit of the register (Rm) by the specified amount.
  eg/ ROR #5
    all bits moved 5 places to the right (i.e. into less significant positions).
  However, rather than being discarded the bits shifted out are then rotated back to other high of the register
    in ROR the bit previously at [0] is rotated to the MSB, [31]
    In RRX - Carry flag included as a 33rd bit in the operation. Bit 0 becomes the Carry out, while the C becomes the MSB
RRX actually encoded as ROR #0
  Example of use: in random number generator given in datasheet
.

## Slide 19: Loading full 32 bit constants
Although the MOV/MVN mechansim will load a large range of constants into a register, sometimes this mechansim will not generate the required constant.
Therefore, the assembler also provides a method which will load ANY 32 bit constant:
  LDR rd,=numeric constant
If the constant can be constructed using either a MOV or MVN then this will be the instruction actually generated.
Otherwise, the assembler will produce an LDR instruction with a PC-relative address to read the constant from a literal pool.
  LDR r0,=0x42 ; generates MOV r0,#0x42
  LDR r0,=0x55555555 ; generate LDR r0,[pc, offset to lit pool]
As this mechanism will always generate the best instruction for a given case, it is the recommended way of loading constants.
Notes: Literal pools
  These are constant data areas embedded in the code at the end of modules, and between functions if required by the user.

## Slide 20: Multiplication Instructions
The Basic ARM provides two multiplication instructions.
Multiply
  MUL{<cond>}{S} Rd, Rm, Rs ; Rd = Rm * Rs
Multiply Accumulate - does addition for free
  MLA{<cond>}{S} Rd, Rm, Rs,Rn ; Rd = (Rm * Rs) + Rn
Restrictions on use:
  Rd and Rm cannot be the same register
    Can be avoid by swapping Rm and Rs around. This works because multiplication is commutative.
  Cannot use PC.
These will be picked up by the assembler if overlooked.
Operands can be considered signed or unsigned
  Up to user to interpret correctly.
Notes: One example of use of MLA is for string to number conversion:
eg/
  Convert string=“123” to value=123
  value = 0
  loop = 0
  len = length of string
  while loop <> len
  c = extract( string, len -loop,1)
  Rm = 10 ^ loop
  Rs = ASC(c) - ASC (‘0’)
  Rd = value
  MLA Rd, Rm, Rs, Rd
  loop = loop + 1
  endwhile

## Slide 21: Load / Store Instructions
The ARM is a Load / Store Architecture:
  Does not support memory to memory data processing operations.
  Must move data values into registers before using them.
This might sound inefficient, but in practice isn’t:
  Load data values from memory into registers.
  Process data in registers using a number of data processing instructions which are not slowed down by memory access.
  Store results from registers out to memory.
The ARM has three sets of instructions which interact with main memory. These are:
  Single register data transfer (LDR / STR).
  Block data transfer (LDM/STM).
  Single Data Swap (SWP).
Notes: All instructions other than these can only use values in registers

## Slide 22: Single register data transfer
The basic load and store instructions are:
  Load and Store Word or Byte
    LDR / STR / LDRB / STRB
ARM Architecture Version 4 also adds support for halfwords and signed data.
  Load and Store Halfword
    LDRH / STRH
  Load Signed Byte or Halfword - load value and sign extend it to 32 bits.
    LDRSB / LDRSH
All of these instructions can be conditionally executed by inserting the appropriate condition code after STR / LDR.
  e.g. LDREQB
Syntax:
  <LDR|STR>{<cond>}{<size>} Rd, <address>

## Slide 23: Stacks
A stack is an area of memory which grows as new data is “pushed” onto the “top” of it, and shrinks as data is “popped” off the top.
Two pointers define the current limits of the stack.
  A base pointer
    used to point to the “bottom” of the stack (the first location).
  A stack pointer
    used to point the current “top” of the stack.
SP BASE
PUSH {1,2,3}
1
2
3
BASE
SP
POP
1
2
Result of pop = 3
BASE
SP

## Slide 24: Stack Operation
Traditionally, a stack grows down in memory, with the last “pushed” value at the lowest address. The ARM also supports ascending stacks, where the stack structure grows up through memory.
The value of the stack pointer can either:
  Point to the last occupied address (Full stack)
    and so needs pre-decrementing (ie before the push)
  Point to the next occupied address (Empty stack)
    and so needs post-decrementing (ie after the push)
The stack type to be used is given by the postfix to the instruction:
  STMFD / LDMFD : Full Descending stack
  STMFA / LDMFA : Full Ascending stack.
  STMED / LDMED : Empty Descending stack
  STMEA / LDMEA : Empty Ascending stack
Note: ARM Compiler will always use a Full descending stack.

## Slide 25: Stack Examples
STMFD sp!, {r0,r1,r3-r5}
r5
r4
r3
r1
r0
SP
Old SP
STMED sp!, {r0,r1,r3-r5}
r5
r4
r3
r1
r0
SP
Old SP
r5
r4
r3
r1
r0
STMFA sp!, {r0,r1,r3-r5}
SP
Old SP
0x400
0x418
0x3e8
STMEA sp!, {r0,r1,r3-r5}
r5
r4
r3
r1
r0
SP
Old SP
Notes:   Lowest register mapped to lowest memory address.
  ‘!’ causes stack pointer updated in all these cases.

## Slide 26: Swap and Swap Byte Instructions
Atomic operation of a memory read followed by a memory write which moves byte or word quantities between registers and memory.
Syntax:
  SWP{<cond>}{B} Rd, Rm, [Rn]
Thus to implement an actual swap of contents make Rd = Rm.
The compiler cannot produce this instruction.
Rm
Rd
Rn
3
2
1
temp
Memory
Notes: Used to move a byte or word quantity from a source register (Rm) to external memory, located by base register Rn
Stores the old memory contents in the destination register (Rd).
Instruction is indivisible - LOCK output goes high to signify to an external MMU or processors that the instruction is uninterruptable.
SWP is used to implement semaphores providing a mutual exclusion between the processor and other devices trying to access memory - originally added by Acorn for use in a multiprocessor system.

## Slide 27: Reference Book
ARM System Developer’s Guide
Designing and Optimizing System Software