## Slide 1: Measurements and instrumentation
Module 6

## Slide 2: 1. Classification of Instruments

## Slide 3: Classification of Instruments
Absolute instruments
Secondary instruments
Digital instruments
Analog instruments
Classified according to quantity they measure
Classified according to kind of current that can be measurand
Classified according to way the output is presented to the user
Indicating instruments
Recording instruments
Integrating instruments
Classified according to method used for comparison
Direct measuring
Comparison
Classified according to their accuracy class
Classified according to which of the effects is used for working

## Slide 4: 2. Working principle of PMMC
PMMC - Permanent Magnet Moving Coil

## Slide 5: 3. MI Instruments
MI – Moving Iron

## Slide 6: 4. Ammeter and Voltmeter

## Slide 7
Measuring current, voltage, and resistance
A
Ammeter:
measures current (A)
connected in series
(current must go through instrument)
I
V
a
b
Voltmeter:
measures potential difference (V)
connected in parallel
Ohmmeter:
measures resistance of an isolated resistor (not in a working circuit)


## Slide 8
Effect of ammeter on circuit
V
R
Measuring current in a simple circuit:
A
connect ammeter in series
Are we measuring the correct current?
(the current in the circuit without ammeter)

## Slide 9
current without the ammeter would be
V
R
Measuring current in a simple circuit:
To minimize error, ammeter resistance r must be very small.
(ideal ammeter would have zero resistance)
any ammeter has some resistance r.
r
connect ammeter in series
Are we measuring the correct current?
(the current in the circuit without ammeter)
current in presence of ammeter is
Effect of ammeter on circuit

## Slide 10
Example: an ammeter of resistance 10 m is used to measure the current through a 10  resistor in series with a 3 V battery that has an internal resistance of 0.5 . What is the relative (percent) error caused by the ammeter?
V=3 V
R=10 
r=0.5 
Actual current without ammeter:
You might see the symbol  used instead of V.

## Slide 11
V=3 V
R=10 
r=0.5 
Current with ammeter:
RA

## Slide 12
Designing an ammeter
ammeter can be based on galvanometer
(for electronic instrument, use electronic sensor instead, analysis still applies)
simplest case: send current directly through galvanometer, observe deflection of needle
Needle deflection is proportional to current. Each galvanometer has a certain maximum current corresponding to full needle deflection.
What if you need to measure a larger current?
use shunt resistor

## Slide 13
Ammeter uses a galvanometer and a shunt, connected in parallel:
A
I

Everything inside the green box is the ammeter.
Current I gets split into Ishunt and IG
Homework hint:
If your galvanometer reads 1A full scale but you want the ammeter to read 5A full scale, then RSHUNT must result in IG=1A when I=5A. What are ISHUNT and VSHUNT?
G
RG
RSHUNT
IG
ISHUNT
I
A
B
galvanometer

## Slide 14
G
RG
RSHUNT
IG
ISHUNT
I
A
B
Shunt also reduces resistance of the ammeter:

## Slide 15
A galvanometer-based ammeter uses a galvanometer and a shunt, connected in parallel:
G
RG
RS
IG
IS
I
Example: what shunt resistance is required for an ammeter to have a resistance of 10 m, if the galvanometer resistance is 60 ?
(actually 0.010002 )
To achieve such a small resistance, the shunt is probably a large-diameter wire or solid piece of metal.

## Slide 16
extra current changes voltage drop across r and thus Vab
To minimize error, voltmeter resistance r must be very large.
(ideal voltmeter would have infinite resistance)
voltmeter has some resistance RV
current IV flows through voltmeter
Effect of voltmeter on circuit
Measuring voltage (potential difference) Vab in a simple circuit:
connect voltmeter in parallel
Are we measuring the correct voltage?
(the voltage in the circuit without voltmeter)
=3 V
R=10 
r=0.5 
RV
a
b
IV

## Slide 17
Example: a galvanometer of resistance 60  is used to measure the voltage drop across a 10 k resistor in series with an ideal 6 V battery and a 5 k resistor. What is the relative error caused by the nonzero resistance of the galvanometer?
Actual voltage drop without instrument:
V=6 V
R1=10 k
R2=5 k
a
b

## Slide 18
The measurement is made with the galvanometer.
V=6 V
R1=10 k
R2=5 k
G
RG=60 
a
b
60  and 10 k resistors in parallel are equivalent to 59.6  resistor.
Total equivalent resistance: 5059.6 
Total current: I=1.186x10-3 A
I=1.19 mA
Vab = 6V – IR2 = 0.07 V.
The relative error is:
Would you pay for this voltmeter?
Would you pay for this voltmeter?
We need a better instrument!

## Slide 19
Example: a voltmeter of resistance 100 k is used to measure the voltage drop across a 10 k resistor in series with an ideal 6 V battery and a 5 k resistor. What is the percent error caused by the nonzero resistance of the voltmeter?
We already calculated the actual voltage drop (2 slides back).
V=6 V
R1=10 k
R2=5 k
a
b

## Slide 20
The measurement is now made with the “better” voltmeter.
V=6 V
R1=10 k
R2=5 k
V
RV=100 k
a
b
100 k and 10 k resistors in parallel are equivalent to an 9090  resistor.
Total equivalent resistance: 14090 
Total current: I=4.26x10-4 A
I=.426 mA
The voltage drop from a to b:
6-(4.26x10-4)(5000)=3.87 V.
The percent error is.
Not great, but much better.

## Slide 21
voltmeter must have a very large resistance
voltmeter can be made from galvanometer in series with a large resistance
V
G
RG
RSer

Everything inside the blue box is the voltmeter.
a
b
Vab
a
b
Vab
Homework hints: “the galvanometer reads 1A full scale” would mean a current of IG=1A would produce a full-scale deflection of the galvanometer needle.
If you want the voltmeter shown to read 10V full scale, then the selected RSer must result in IG=1A when Vab=10V.
Homework hints: “the galvanometer reads 1A full scale” would mean a current of IG=1A would produce a full-scale deflection of the galvanometer needle.
If you want the voltmeter shown to read 10V full scale, then the selected RSer must result in IG=1A when Vab=10V.
Designing a voltmeter

## Slide 22: 5. Digital multimeters

## Slide 23: What is a multimeter?
A multimeter is a devise used to measure voltage, resistance and current in electronics & electrical equipment
It is also used to test continuity between to 2 points to verify if there is any breaks in circuit or line
There are two types of multimeter Analog & Digital
  Analog has a needle style gauge
  Digital has a LCD display (Referenced during this PPT)

## Slide 24
Switched
Manually switch between ranges to get most accurate reading.
Auto Range Switches between ranges automatically for best reading.
There are 2 styles of multimeters
Both of these styles work the same

## Slide 25
Meter leads
Red meter lead Is connected to Voltage/Resistance or amperage port Is considered the positive connection
Black meter lead Is always connected to the common port Is considered the negative connection
Probes Are the handles used to hold tip on the tested connection
Tips Are at the end of the probe and provides a connection point

## Slide 26: Display & Dial Settings
Meter Dial Turn dial to change functions. Turn dial to OFF position after use.
Panel Indicator Shows each function and setting range to turn dial to.
Probe Connections Specific for each function.
Digital Display Shows measured value.

## Slide 27: Common DMM Symbols
~ AC Voltage Ground
--- DC Voltage ( Capacitor
Hz Hertz mF MicroFarad
+ Positive m Micro
Negative m Milli
W Ohms M Mega
* Diode K Kilo
))) Audible Continuity OL Overload
These symbols are often found on multimeter and schematics.
They are designed to symbolize components and reference values.

## Slide 28: Measuring Voltage
Voltage (V) is the unit of electrical pressure; one volt is the potential difference needed to cause one amp of current to pass through one ohm of resistance
Voltage is broke up into 2 sections AC & DC
Alternating Current (AC) is house voltage (110vac)
Direct Current (DC) is battery voltage (12vdc)
On switched meters use one value higher than your expected value
Be very careful to not touch any other electronic components within the equipment and do not touch the tips to each other while connected to anything else
To measure voltage connect the leads in parallel between the two points where the measurement is to be made. The multimeter provides a parallel pathway so it needs to be of a high resistance to allow as little current flow through it as possible

## Slide 29: Measuring Voltage

## Slide 30
Measuring Voltage
9.0vdc

## Slide 31: Measuring Resistance and Continuity
Resistance (W) is the opposition to current
Resistance is measured in Ohm's
Disconnect power source before testing
Remove component or part from system before testing
Measure using lowest value, if OL move to next level
Testing for continuity is used to test to verify if a circuit, wire or fuse is complete with no open
Audible continuity allows an alarm if circuit is complete
If there is no audible alarm resistance of 1ohm to .1ohm should be present

## Slide 32: Measuring Resistance

## Slide 33: Measuring or Testing Continuity

## Slide 34: Measuring Resistance
100W

## Slide 35: Measuring Continuity
5 amp
Fuse
.5W

## Slide 36
Current (amps) is the flow of electrical charge though a component or conductor
Current is measured in amps or amperes
Disconnect power source before testing
Disconnect completed circuit at end of circuit
Place multimeter in series with circuit
Reconnect power source and turn ON
Select highest current setting and work your way down.
Measuring Current

## Slide 37
Measuring Current

## Slide 38
Measuring Current
1.1amps

## Slide 39: overview
A meter capable of checking for voltage, current, and resistance is called a multimeter,
When measuring Voltage the multimeter must be connected to two points in a circuit in order to obtain a good reading. Be careful not to touch the bare probe tips together while measuring voltage, as this will create a short-circuit!
Never read Resistance or test for Continuity with a multimeter on a circuit that is energized.
When measuring Current the multimeter must be connected in a circuit so the electrons have to flow through the meter
Multimeters have practically no resistance between their leads. This is intended to allow electrons to flow through the meter with the least possible difficulty. If this were not the case, the meter would add extra resistance in the circuit, thereby affecting the current