## Slide 1: Complete reference material for “module 1”

## Slide 2: Basic circuit elements and sources, Ohms law
Date: 13-07-2020
Module 1: Fundamentals of DC Circuits
EEE 1024 Fundamentals of Electrical and Electronics Engineering

## Slide 3: Biography
Dr. Kishore Bingi
Assistant Professor Senior Grade 1
School of Electrical Engineering
PhD from Universiti Teknologi PETRONAS, Malaysia
https://www.kishorebingi.co.in/
kishore.bingi@vit.ac.in

## Slide 4: Microsoft Teams & Others
Team Name: EEE1024 A1/A2 Slot Monday & Wednesday Morning
Syllabus: Teams - General – Files
Material: Teams – Module – Files
Attendance: Teams – Time in & Time Out – VTOP
Questions during Presentation: Raise Hand
Queries in General: Teams – Channel – Chat
Assignments – End of each module through Moodle

## Slide 5: Topics
Electrical Circuit
Circuit Elements
Charge
Electrical Current
Electrical Voltage
Power & Energy
Resistors and Ohm’s Law
Ohm’s Law Triangle
Power Triangle
Ohm’s Law Pie Chart

## Slide 6: Electrical Circuit
An electrical circuit consists of various types of circuit elements connected in closed paths by conductors.
The circuit elements can be resistances, inductances, capacitances, and voltage sources, among others

## Slide 7: Charge
Charge flows easily through conductors, which are represented by lines connecting circuit elements.
Voltage sources create forces that cause charge to flow through the conductors and other circuit elements.
As a result, energy is transferred between the circuit elements, resulting in a useful function.

## Slide 8: Electrical Current
Electrical current is the time rate of flow of electrical charge () through a conductor or circuit element.
The units are amperes (A), which are equivalent to coulombs per second (C/s).
The charge on an electron is C.
To find charge given current, we must integrate.
is some initial time at which the charge is known.

## Slide 9: example 1: Determining Current Given Charge
Suppose that charge versus time for a circuit element is given by
Calculate and Plot and
Solution:
For
For

## Slide 10: Assignment 1: Determining Current Given Charge
The charge that passes through a circuit element is given by
Find the current as a function of time.

## Slide 11: Direct Current (DC) and Alternating Current (AC)
When a current is constant with time, we say that we have direct current, abbreviated as dc
When current that varies with time, reversing direction periodically, is called alternating current, abbreviated as ac.
?

## Slide 12: Direct Voltage (DC) and Alternating Voltage (AC)
The voltage associated with a circuit element is the energy transferred per unit of charge that flows through the element.
The units of voltage are volts (V), which are equivalent to joules per coulomb (J/C).
Voltage constant with time is called dc voltage.
Voltage that change in magnitude and alternate in polarity with time is called ac voltage.

## Slide 13: Basic Circuit Elements
Resistance
Inductance
Capacitor
Sources
Voltage (V or J/C) – dc & ac
Current (A or C/s) – dc & ac

## Slide 14: Power & energy
The current i is the rate of flow of charge and the voltage v is a measure of the energy transferred per unit of charge, the product of the current and the voltage is the rate of energy transfer.
Thus, the product of current and voltage is power.
Volts * Amperes = (joules/coulomb) * (coulombs/second) = joules/second = watts

## Slide 15: Power & energy
To calculate the energy delivered to a circuit element between time instants and , we integrate power
The units of energy is joules (J)

## Slide 16: Example 3 & 4: Energy & Power
Voltage is 12V and Current is 2 A. Calculate the power
Voltage is 12V and Current is Calculate the power and energy for the intervals from to
Energy:

## Slide 17: Resistors and Ohm’s Law
The relationship between Voltage, Current and Resistance in any DC electrical circuit was firstly discovered by the German physicist Georg Ohm.
The voltage V across an ideal resistor is proportional to the current I through the resistor R.
The units of resistance are V/A, which are called ohms. The uppercase Greek letter omega (Ω) represents ohms.

## Slide 18: Ohms Law Triangle

## Slide 19: Power Triangle

## Slide 20: Ohms Law Pie Chart

## Slide 21: Assignment 2: Match the following
Units of Voltage
Units of Current
Units of Power
Units of Resistance
Units of Charge
Units of Energy
Units of Conductance
Ohm’s law
Power
Resistivity
Watt
V=I*R
Ohm (Ω)
Ampere (A or C/s)
Volt (V or J/C)
P=V*I
Siemens (S)
(R*A)/L
Joules (J)
C

## Slide 22: Conductance
Solving Ohm’s law for current, we have
We call the quantity a conductance.
It is customary to denote conductance with the letter G.
Conductance's have the units of inverse ohms (), which are called siemens (abbreviated S). Thus, we can write Ohm’s law as

## Slide 23: Resistance Related to Physical Parameters
The cross-sectional area A is constant along the length of the cylinder or bar. If the length L of the resistor is much greater than the dimensions of its cross section, the resistance is approximately given by
is the resistivity of the material used to construct the resistor.
The units of resistivity are ohm meters (Ωm)

## Slide 24: Resistance Related to Physical Parameters
Materials can be classified as conductors, semiconductors, or insulators, depending on their resistivity.
Conductors have the lowest resistivity and easily conduct electrical current.
Insulators have very high resistivity and conduct very little current (at least for moderate voltages).
Semiconductors fall between conductors and insulators.

## Slide 25
Insulator
conductors
semiconductors

## Slide 26: Assignment 1: Resistance Calculation
Compute the resistance of a copper wire having a diameter of 2.05 mm and a length of 10 m. Note the resistivity of a copper is given as m.

## Slide 27: Kirchhoff’s laws
Date: 15-07-2020
Module 1: Fundamentals of DC Circuits
EEE 1024 Fundamentals of Electrical and Electronics Engineering

## Slide 28: Node
A node in an electrical circuit is a point at which two or more circuit elements are joined together.

## Slide 29: Kirchhoff’s laws
Kirchhoff’s Current Law
Kirchhoff’s Voltage Law

## Slide 30: Kirchhoff’s Current Law
Kirchhoff’s current law: The net current entering a node is zero.
To compute the net current entering a node, we add the currents entering and subtract the currents leaving.
Node a:
Node b:
Node c:

## Slide 31: Kirchhoff’s Current Law
We abbreviate Kirchhoff’s current law as KCL.
Another way to state KCL is: The sum of the currents entering a node equals the sum of the currents leaving a node.
Node a:
Node b:
Node c:

## Slide 32: Kirchhoff’s Current Law
All points in a circuit that are connected directly by conductors can be considered as a single node.
For example, in Figure, elements A, B, C, and D are connected to a common node.
Applying KCL, we can write

## Slide 33: Series Circuits
When elements are connected end to end, we say that they are connected in series.
For elements A and B to be in series, no other path for current can be connected to the node joining A and B.
KCL at Node 1:
KCL at Node 2:
Thus,
Thus, all elements in a series circuit have identical currents.

## Slide 34: Example: KCL
Which elements are in series?
What is the relationship between id and ic?
Given that ia = 6 A and ic = -2 A, determine the values of ib and id.

## Slide 35: Example: KCL
Identify the groups of circuit elements that are connected in series.
Use KCL to determine the values of the unknown currents

## Slide 36: Example: KCL
Find the values of the branch currents using KCL
For the constant node current 3A, what will happen if ‘C’ is removed?

## Slide 37: Kirchhoff’s Voltage Law
Loop: A loop in an electrical circuit is a closed path starting at a node and proceeding through circuit elements, eventually returning to the starting node.

## Slide 38: Kirchhoff’s voltage law (KVL)
The algebraic sum of the voltages equals zero for any closed path (loop) in an electrical circuit.
In traveling around a loop, we encounter various voltages, some of which carry a positive sign while others carry a negative sign in the algebraic sum.
A convenient convention is to use the first polarity mark encountered for each voltage to decide if it should be added or subtracted in the algebraic sum.
Loop 1:
Loop 2:
Loop 3:

## Slide 39: Parallel Circuits
We say that two circuit elements are connected in parallel if both ends of one element are connected directly (i.e., by conductors) to corresponding ends of the other.
Element B is not in parallel with D because the top end of B is not directly connected to the top end of D.

## Slide 40: Kirchhoff’s Voltage Law
Loop 1:
Loop 2:
Loop 3:
Thus, =
Thus, in parallel circuits, the magnitudes and actual polarities of all three voltages are the same.

## Slide 41: Example: kvl
Which elements are in parallel?
Which elements are in series?
What is the relationship between vd and vf?
Given that va = 10 V, vc = 15 V, and ve = 20 V, determine the values of vb and vf.

## Slide 42: Assignment 2: kvl
Identify the elements that are in parallel
Identify the elements that are in series
Find the values of vc and ve

## Slide 43: Assignment 3: KCL & kvl
Find the values of the other currents in Figure, if ia = 1 A, ib = 2 A, id = -3 A, and ih = 5 A.

## Slide 44: Assignment 4: KCL & kvl
Solve for the other voltage shown in Figure, given that va = 10 V, vb = 8 V, vf = -5 V, and vh = 2 V.

## Slide 45: Thank you 
Nodes?
Elements in Parallel?
Elements in Series?

## Slide 46: Problems on Ohm’s law, KCL & KVL
Module 1: Fundamentals of DC Circuits
EEE1024 Fundamentals of Electrical and Electronics Engineering

## Slide 47: Current & charge
Current is the time rate of flow of electrical charge. Its units are amperes (A), which are equivalent to coulombs per second (C/s)
1. The current through a given circuit element is given by
Find the net charge that passes through the element in the interval for t = 0 to t = ∞.
2. The net charge through a cross section of a certain circuit element is given by
Determine the current through the element.

## Slide 48: Power & energy
3. Consider the element shown in Figure, which has v(t) = −15 V and i(t) = A.
Compute the power for the circuit element.
Find the energy transferred between t =0 and t=∞.
Is this energy absorbed by the element or supplied by it?

## Slide 49: KCL
4. Given that ib = 3 A; ic = 5 A; ig = 6 A, and ie = 5 A, determine the values of other currents
5. Determine the values of the other currents in Figure, given that ia = 2A, ic = −3A, ig = 6A, and ih = 1A.

## Slide 50: KVL
6. We know that va = 10 V, vb = −3 V, vf = 12 V, and vh = 5 V, solve for the other voltages

## Slide 51: Ohm’s law, kcl & kvl
7. Consider the circuit shown in Figure, Use repeated applications of Ohm’s law, KVL, and KCL to eventually find Vx.

## Slide 52: Ohm’s law, kcl & kvl
8. Use repeated applications of Ohm’s law, KVL, and KCL to eventually find the value of Ix in the circuit

## Slide 53: Node voltage analysis
Module 1: Fundamentals of DC Circuits
EEE1024 Fundamentals of Electrical and Electronics Engineering

## Slide 54: Ohm’s law, kcl & kvl
1. Consider the circuit shown in Figure, Use repeated applications of Ohm’s law, KVL, and KCL to eventually find Vx.

## Slide 55: Ohm’s law, kcl & kvl
2. Use repeated applications of Ohm’s law, KVL, and KCL to eventually find the value of Ix in the circuit
Assignment 1

## Slide 56: Resistance's in series and Parallel

## Slide 57: Series Resistances
Consider the series combination of three resistances shown in Figure.
Recall that in a series circuit the elements are connected end to end and that the same current flows through all the elements.
Using KVL
Using Ohm’s Law

## Slide 58: Parallel elements
Figure shows three resistances in parallel.
In a parallel circuit, the voltage across each element is the same.
Using KCL at top node
Using Ohm’s Law

## Slide 59: Combining Resistances in Series and Parallel
Find a single equivalent resistance for the network shown in Figure

## Slide 60: node-voltage analysis

## Slide 61: Can we apply KCL, KVl and Other ???

## Slide 62: node-voltage analysis

## Slide 63: Example 1
Write equations and solve for the node voltages shown in Figure. Then, find the value of i1.

## Slide 64: Example 2
Solve for the node voltages shown in Figure.
What are the new values of the node voltages after the direction of the current source is reversed?
How are the values related?

## Slide 65: Example 3
Find Node Voltages and then find ix

## Slide 66: Assignment 1
Given R1 = 20, R2 = 8, R3 = 20, R4 = 12, R5 = 10, R6 = 5, and Is = 4 A.
Solve for the node voltages shown in Figure

## Slide 67: Assignment 2
Given R1 = 4, R2 = 5, R3 = 8, R4 = 6, R5 = 8 and Is = 4 A,
Solve for the node voltages shown in Figure

## Slide 68: Mesh-Current Analysis

## Slide 69: Branch & mesh currents

## Slide 70: Choosing the Mesh Currents

## Slide 71: Branch Currents
Current in R1: i3
Current in R2: (i1-i3) or (i3-i1)
Current in R3: (i1-i2) or (i2-i1)
Current in R4: i2

## Slide 72: Choosing the Mesh Currents

## Slide 73: Branch Currents
Current in R1: i1
Current in R2: (i1-i4) or (i4-i1)
Current in R3: i4
Current in R4: (i1-i2) or (i2-i1)
Current in R5: i2
Current in R6: (i2-i3) or (i3-i2)
Current in R7: i3
Current in R8: (i3-i4) or (i4-i3)

## Slide 74: Procedure
Step 1: To select the mesh currents to flow clockwise.
Step 2: Then, we write a KVL equation for each mesh, going around the meshes clockwise.
Note: As usual, we add a voltage if its positive reference is encountered first in traveling around the mesh, and we subtract the voltage if the negative reference is encountered first.

## Slide 75: Mesh-Current Equations using KVl
Loop 1:
-va + (i1-i3)R2 + (i1-i2)R3 = 0
Loop 2:
R3(i2-i1) + vb + R4(i2) = 0
Loop 3:
R2(i3-i1) + R4(i3) – vb = 0

## Slide 76: MESH-CURRENT ANALYSIS
Date: 27-07-2020
Module 1: Fundamentals of DC Circuits
EEE 1024 Fundamentals of Electrical and Electronics Engineering

## Slide 77: Example 1
Solve for the current in each element of the circuit shown in Figure

## Slide 78: Example 2
Write Mesh-Current Equations in Matrix form

## Slide 79: Example 3 - Mesh Currents in Circuits Containing Current Sources
Solve for mesh-currents

## Slide 80: Example 4
Solve for Mesh Currents

## Slide 81: Example 5
Solve for the power delivered to the 24 Ohms resistor and for the mesh currents shown in Figure

## Slide 82: Example 6
Use mesh-current analysis to find the value of i1 in the circuit of Figure

## Slide 83: Example 7
Solve for the power delivered by the voltage source in Figure, using the mesh current method.

## Slide 84: Example 8
Use mesh-current analysis to determine the voltage magnitude for each resistor

## Slide 85: Thevenin's and Maximum Power Transfer Theorem
Module 1: Fundamentals of DC Circuits
EEE1024 Fundamentals of Electrical and Electronics Engineering

## Slide 86: module 1
Current & Charge
Voltage, Power & Energy – Power Triangle
Ohm’s Law – Ohm’s Law Triangle & Pie Chart
KCL
Node
KCL Law
Series Elements
KVL
Loop
KVL Law
Parallel Elements
Equivalent Resistances of Series and Parallel Resistances
Node-Voltage Analysis
Mesh-Current Analysis
Thevenin’s Theorem
Maximum Power Transfer

## Slide 87: Thevenin’s theorem
Here, we learn how to replace two-terminal circuits containing resistances and sources by simple equivalent circuits.
By a two-terminal circuit, we mean that the original circuit has only two points that can be connected to other circuits.

## Slide 88: Thevenin Equivalent Circuit
One type of equivalent circuit is the Thevenin equivalent, which consists of an independent voltage source in series with a resistance
Vt is Thevenin’s Voltage
Rt is Thevenin’s Resistance

## Slide 89: Thevenin Equivalent Circuit
According to the Theorem, the Thevenin source voltage Vt is equal to the open-circuit voltage of the original network.
Furthermore, the current flowing in this circuit is

## Slide 90: Ex 1: Determining the Thevenin Equivalent Circuit

## Slide 91: Finding the ThEvenin Resistance Directly
There is an alternative way to find the Thévenin resistance.
First, we zero the sources in the network.
In zeroing a voltage source, we reduce its voltage to zero. A voltage source with zero voltage is equivalent to a short circuit.
In zeroing a current source, we reduce its current to zero. By definition, an element that always carries zero current is an open circuit.
Thus, to zero the sources, we replace voltage sources with short circuits and replace current sources with open circuits.

## Slide 92: Ex 2: Finding the ThEvenin Resistance Directly

## Slide 93: Ex 3: Finding the ThEvenin Resistance Directly

## Slide 94: Ex 4: Finding the ThEvenin Equivalent Circuit

## Slide 95: Ex 5: Finding the ThEvenin Resistance Directly
Find the Thévenin resistance for each of the circuits shown in Figure by zeroing the sources.

## Slide 96: Maximum Power Transfer

## Slide 97
Suppose that we have a two-terminal circuit and we want to connect a load resistance RL such that the maximum possible power is delivered to the load. This is illustrated in Figure
To analyse this problem, we replace the original circuit by its Thevenin equivalent as shown in Figure. The current flowing through the load resistance is given by
The power delivered to the load is
Substituting Current,

## Slide 98: Maximum Power Transfer
To find the value of the load resistance that maximizes the power delivered to the load, we set the derivative of pL with respect to RL equal to zero:
Solving for the load resistance, we have
Thus, the load resistance that absorbs the maximum power from a two-terminal circuit is equal to the Thevenin resistance.
 

## Slide 99: Ex 6: Determining Maximum Power Transfer
Find the load resistance for maximum power transfer from the circuit shown in Figure. Also, find the maximum power.

## Slide 100: End of module 1

## Slide 101: Quiz for module 1