## Slide 1: Assembly Language Programming

## Slide 2
Instruction Opcode Description
LOAD MQ 00001010 AC ← MQ
LOAD MQ, M(X) 00001001 MQ ← M(X)
STOR M(X) 00100001 M(X) ← AC
LOAD M(X) 00000001 AC ← M(X)
LOAD – M(X) 00000010 AC ← – M(X)
LOAD |M(X)| 00000011 AC ← |M(X)|
LOAD – |M(X)| 00000100 AC ← – |M(X)|

## Slide 3
Instruction Opcode Description
JUMP M(X,0:19) 00001101 next instruction M(X,0:19)
JUMP M(X,20:39) 00001110 next instruction
M(X,20:39)

## Slide 4
Instruction Opcode Description
JUMP +M(X,0:19) 00001111 IF AC ≥ 0, then next instruction M(X,0:19)
JUMP +M(X,20:39) 00010000 IF AC ≥ 0, then next instruction
M(X,20:39)

## Slide 5
Instruction Opcode Description
ADD M(X) 00000101 AC ← AC+M(X)
ADD |M(X)| 00000111 AC ← AC+|M(X)|
SUB M(X) 00000110 AC ← AC─M(X)
SUB |M(X)| 00001000 AC ← AC ─ |M(X)|
MUL M(X) 00001011 AC, MQ ← MQ×M(X)
DIV M(X) 00001100 MQ, AC ← MQ/M(X)
LSH 00010100 AC ← AC x 2
RSH 00010101 AC ← AC / 2

## Slide 6
Instruction Opcode Description
STOR M(X,8:19) 00010010 M(X,8:19) ← AC(28:39)
STOR M(X,28:39) 00010011 M(X,28:39) ← AC(28:39)

## Slide 7: ALP
Write an appropriate assembly language code for the following operation and interpret to Von Neumann IAS architecture
X=Y*Z
Where Z->40 bit data and Y->40 bit data
Result would be more than 40 bit.

## Slide 8
Assume that data variables ‘Y’ & ‘Z’ available at memory locations 801 & 802 respectively. And X will be stored 803 onwards.
LOAD MQ, M(801) MQM[801]
MUL M(802) AcMQ * M[802]
STOR M(803) M[803]Ac
LOAD MQ AcMQ
STOR M(804) M[804]Ac

## Slide 9
Write an assembly language program to perform A= (B-C) * D
Assumption: Inputs are available 801 onwards
Load M(801)
Sub M(802)
Stor M(804)
Load MQ, M(804)
Mul M(803)
Stor M(804)
Load MQ
Stor M(805)

## Slide 10
Write an ALP for the following
If a>0
a=a-b
else
a=a+b

## Slide 11
Assume:
[100]a [101]b [100]a+b/a-b
1 LOAD M(100), JMP +M(3,0:19)
2 ADD M(101), JMP M(3,20:39)
3 SUB M(101), STOR M(100)

## Slide 12
Write an assembly language program to perform X=(A+B) * (C+D)
Y=(A-B)/[C+(D/E)]