## Slide 1: Module 2
Instruction Format

## Slide 2: Instruction Format
The instruction is divided into two fields
  Opcode field
  Operand field
This operand field further divided into one to four fields.
Simple instruction format
Opcode
Operand
Address1
Operand
Address2
Result
Address1
Next
Instruction

## Slide 3
Instruction Set is categorized into types based on
  Operation performed
  number of operand addresses
  and addressing modes
Based on Operation
Data Movement
  Memory : LOAD, STORE, MOV I\O Instructions: IN, OUT
Data Processing
  Arithmetic : Add, Sub, MUL Logic Instructions: AND, OR,
Control Instructions
  Conditional : JNZ, JZ Un Conditional: Jump

## Slide 4
Based on number of operand address in the instruction.
    4 Address Instruction
    3 Address Instruction
    2 Address Instruction
    1 Address Instruction
    0 Address Instruction
For a two-operand arithmetic instruction, five items need to be specified
  Operation to be performed (opcode)
  Location of the first operand
  Location of the second operand
  Place to store the result
  Location of next instruction to be executed

## Slide 5: Assumptions 24-bit memory address (3 bytes) 128 instructions (7 bits rounded to 1 byte)

## Slide 6: 4- Address Instruction
24 Bits / 3 Bytes
Memory
Op Code
ResAddr
Op1Addr
Op2Addr
NextiAddr
8
24
24
24
24
+
CPU
Op Code
ResAddr
Op1Addr
Op2Addr
NextiAddr
Op1
Op2
Resop
Example: add M1,M2,M3, nexti
M(1)M(2)+M(3)
Memory Required to store an Instruction:
5 x 3 bytes = 15 Bytes
Memory Required to Encode an Instruction:
1Byte+ 4 x 3 bytes = 13 Bytes
Calculation of Memory Accesses
To fetch Instruction itself
Opcode=1
Op1Addr=1
Op2Addr=1
ResAddr=1
NextiAddr=1
Total=5
To Execute an Instruction
Op1=1
Op2=1
Res=1
Total=3
Total Memory Traffic= No. of M/A to fetch + No. of M/A to Execute
Total Memory Traffic= 5 + 3 =8

## Slide 7: 3- Address Instruction
24 Bits / 3 Bytes
Memory
Op Code
ResAddr
Op1Addr
Op2Addr
8
24
24
24
+
CPU
Op Code
ResAddr
Op1Addr
Op2Addr
Op1
Op2
Resop
Example: add M1,M2,M3
M(1)M(2)+M(3)
Memory Required to store an Instruction:
4 x 3 bytes = 12 Bytes
Memory Required to Encode an Instruction:
1Byte+ 3 x 3 bytes = 10 Bytes
Calculation of Memory Accesses
To fetch Instruction itself
Opcode=1
Op1Addr=1
Op2Addr=1
ResAddr=1
Total=4
To Execute an Instruction
Op1=1
Op2=1
Res=1
Total=3
Total Memory Traffic= No. of M/A to fetch + No. of M/A to Execute
Total Memory Traffic= 4+ 3 =7
PC
24

## Slide 8: 2- Address Instruction
24 Bits / 3 Bytes
Memory
Op Code
Op1Addr
Op2Addr
8
24
24
24
+
CPU
Op Code
Op1Addr
Op2Addr
Op1
Op2
Resop
Example: add M2,M3
M(2)M(2)+M(3)
Memory Required to store an Instruction:
3 x 3 bytes = 09 Bytes
Memory Required to Encode an Instruction:
1Byte+ 2 x 3 bytes = 7 Bytes
Calculation of Memory Accesses
To fetch Instruction itself
Opcode=1
Op1Addr=1
Op2Addr=1
Total=3
To Execute an Instruction
Op1=1
Op2=1
Res=1
Total=3
Total Memory Traffic= No. of M/A to fetch + No. of M/A to Execute
Total Memory Traffic= 3+ 3 =6
PC
24

## Slide 9: 1- Address Instruction
24 Bits / 3 Bytes
Memory
Op Code
Op1Addr
8
24
24
+
CPU
Op Code
Op1Addr
Op1
Op2
Resop
Example: add M2
Memory Required to store an Instruction:
2 x 3 bytes = 06 Bytes
Memory Required to Encode an Instruction:
1Byte+ 1 x 3 bytes = 4Bytes
Calculation of Memory Accesses
To fetch Instruction itself
Opcode=1
Op1Addr=1
Total=2
To Execute an Instruction
Op1=1
Total=1
Total Memory Traffic= No. of M/A to fetch + No. of M/A to Execute
Total Memory Traffic= 2+ 1 =3
PC
24
Acc

## Slide 10: 0-Address Instruction

## Slide 11: Comparisons
Instruction Type | Memory To Store in Bytes | Memory To Encode in Bytes | M/As to fetch an Instruction | M/As to Execute an Instruction | Memory Traffic
4-address | 5 x 3 = 15 | 1+(4 x 3) = 13 | 5 | 3 | 5+3=8
3-Address | 4 x 3 = 12 | 1+(3 x 3) = 10 | 4 | 3 | 4+3=7
2-Address | 3 x 3 = 09 | 1+(2 x 3) = 07 | 3 | 3 | 3+3=6
1-Address | 2 x 3 = 06 | 1+(1 x 3) = 04 | 2 | 1 | 2+1=3
0-Address | 1 x 3 = 03 | 1+(0 x 3) = 01 | 1 | 0 | 1+0=1

## Slide 12: Evaluate a = (b+c)*d - e
ab+c
add a, b, c
mpy a, a, d
sub a, a, e
aa*d
aa-e
ab
load a, b
add a, c
mpy a, d
aa+c
aa*d
sub a, e
aa-e
Accb
load b
add c
mpy d
AccAcc+c
AccAcc*d
sub e
AccAcc-e
store a
aAcc
push b
push c
add
push d
mpy
push e
sub
pop a
3-Address
2-Address
1-Address
0-Address
pop a
push a

## Slide 13
ab+c
add a, b, c
mpy a, a, d
sub a, a, e
aa*d
aa-e
ab
load a, b
add a, c
mpy a, d
aa+c
aa*d
sub a, e
aa-e
Memory to Store | Memory to encode | M/As to Fetch | M/As to Execute | Memory Traffic
4*3=12 | 1+(3*3)=10 | 4 | 3 | 4+3=7
4*3=12 | 1+(3*3)=10 | 4 | 3 | 4+3=7
4*3=12 | 1+(3*3)=10 | 4 | 3 | 4+3=7
36 | 30 | 12 | 9 | 21
Memory to Store | Memory to encode | M/As to Fetch | M/As to Execute | Memory Traffic
3*3=9 | 1+(2*3)=7 | 3 | 2 | 3+2=5
3*3=9 | 1+(2*3)=7 | 3 | 3 | 3+3=6
3*3=9 | 1+(2*3)=7 | 3 | 3 | 3+3=6
3*3=9 | 1+(2*3)=7 | 3 | 3 | 3+3=6
36 | 28 | 12 | 11 | 23

## Slide 14
Accb
load b
add c
mpy d
AccAcc+c
AccAcc*d
sub e
AccAcc-e
store a
aAcc
Memory to Store | Memory to encode | M/As to Fetch | M/As to Execute | Memory Traffic
2*3=6 | 1+(1*3)=4 | 2 | 1 | 2+1=3
2*3=6 | 1+(1*3)=4 | 2 | 1 | 2+1=3
2*3=6 | 1+(1*3)=4 | 2 | 1 | 2+1=3
2*3=6 | 1+(1*3)=4 | 2 | 1 | 2+1=3
2*3=6 | 1+(1*3)=4 | 2 | 1 | 2+1=3
30 | 20 | 10 | 5 | 15
6 | 4 | 2 | 1 | 3
3 | 1 | 1 | 0 | 1
39 | 23 | 13 | 5 | 18
push b
push c
add
push d
mpy
push e
sub
pop a

## Slide 15
Evaluate X=(A+B) * (C+D)
Evaluate Y=(A-B)/[C+(D/E)]