## Slide 1
Calculate the effective address for the following addressing modes?
Immediate addressing mode
Add A, #100
Effective address = 100
R=1000, [1000]= 50
Register Direct Addressing Mode
Add R, #50 ; R  R + 50 R 1000+50
EA = R
Add [R],50 R  50+50
EA =[R]

## Slide 2
Register Indirect Add [[R]], 50
R = 1000, [1000] = [2000] = 40
EA =[[R]]
Memory Direct : Add [1000], 50
[1000] = 40
EA =[1000]
Memory Indirect : Add[[1000], 50
[1000] = [2000] = 60
EA = [[1000]]

## Slide 3
Index addressing mode ( SI , DI )
EA = BX / memory location + SI/DI + offset
Bx= 1000, SI = 20 , offset = 3
EA = 1000+ 20 + 3 = 1023  50
Relative addressing mode ( PC) Pc  5000
EA = Pc + SI/DI + offset
Pc =5000, Si = 200, offset = 5
EA = [5205]
Auto increment : [R]+ R  R +1
R = 400= 401
Auto Decremnt : [R]- R  R-1
R= 399

## Slide 4
Program starts from the location 1000.
1000 : Add A, 100
Add [A], 1
Add [R], 2
Add[[R]], 2
Add [1008], 3
Add [[1008]], 4
Add [Bx+Si+offset], 3
add [Pc], 2
Memory location details
Memory Data
0009 6
1002 1008
1008 1100
1100 50
1101 7
1102 9
1103 8
R = 1102, Bx = 1000, SI = 100, offset = 2
Effective address of all the addressing mode.