## Slide 1: Virtual Memory & Replacement Algorithm

## Slide 2: VIRTUAL MEMORY
Give the programmer the illusion that the system has a very large memory,
even though the computer actually has a relatively small main memory
Address Space(Logical) and Memory Space(Physical)
Address Mapping
Memory Mapping Table for Virtual Address -> Physical Address
virtual address
(logical address)
physical address
address space
memory space
address generated by programs actual main memory address
Mapping
Virtual address
Virtual
address
register
Memory
mapping
table
Memory table
buffer register
Main memory
address
register
Main
memory
Main memory
buffer register
Physical
Address
Virtual Memory

## Slide 3: ADDRESS MAPPING
Organization of memory Mapping Table in a paged system
Address Space and Memory Space are each divided
into fixed size group of words called blocks or pages
1K words group
Page 0
Page 1
Page 2
Page 3
Page 4
Page 5
Page 6
Page 7
Block 3
Block 2
Block 1
Block 0
Address space
N = 8K = 213
Memory space
M = 4K = 212
0
000
1
001
1
010
0
011
0
100
1
101
1
110
0
111
1
Block 0
Block 1
Block 2
Block 3
MBR
0 1
0 1 0 1 0 1 0 0 1 1
1 0 1
0 1 0 1 0 1 0 0 1 1
Table
address
Presence
bit
Page no.
Line number
Virtual address
Main memory
address register
Memory page table
Main memory
11
00
01
10
01
Virtual Memory

## Slide 4
Memory Page table consist of Eight words ,one for each page.
The address in the page table denotes the Page number, and the content of the word gives the block number where the page is stored.
A presence bit indicates whether the page has been transferred from auxiliary memory in to main memory
If the page is not there call to the operating system is then generated to fetch the required page from auxiliary memory to main memory

## Slide 5: ASSOCIATIVE MEMORY PAGE TABLE
Assume that
Number of Blocks in memory = m
Number of Pages in Virtual Address Space = n
Page Table
- Straight forward design -> n entry table in memory
Inefficient storage space utilization
<- n-m entries of the table is empty
- More efficient method is m-entry Page Table
Page Table made of an Associative Memory
m words; (Page Number: Block Number)
1 0 1
Line number
Page no.
Argument register
1 1 1 0 0
0 0 1 1 1
0 1 0 0 0
1 0 1 0 1
1 1 0 1 0
Key register
Associative memory
Page no.
Block no.
Virtual address
Page Fault
Page number cannot be found in the Page Table
Virtual Memory

## Slide 6: PAGE REPLACEMENT ALGORITHMS
FIFO
7 0
7
1
7
2
0
3
0
4
2
3
0
3
2
1
2
0
1
7
7
0
1
0
0
1
2
0
1
2
3
1
2
3
0
4
3
0
4
2
0
4
2
3
0
2
3
0
1
3
0
1
2
7
1
2
7
0
2
7
0
1
Page frames
Reference string
-
FIFO algorithm selects the page that has been in memory the longest time
Using a queue - every time a page is loaded, its
identification is inserted in the queue
Easy to implement
May result in a frequent page fault
Optimal Replacement (OPT) - Lowest page fault rate of all algorithms
Replace that page which will not be used for the longest period of time
0
7
1
7
2
0
3
0
4
2
3
0
3
2
1
2
0
1
7
7
0
1
0
0
7
1
2
0
1
2
0
3
2
4
3
2
0
3
2
0
1
7
0
1
Page frames
Reference string
Virtual Memory

## Slide 7: PAGE REPLACEMENT ALGORITHMS
- OPT is difficult to implement since it requires future knowledge
- LRU uses the recent past as an approximation of near future.
Replace that page which has not been
used for the longest period of time
LRU
0
7
1
7
2
0
3
0
4
2
3
0
3
2
1
2
0
1
7
7
0
1
0
0
7
1
2
0
1
2
0
3
4
0
3
4
0
2
4
3
2
0
3
2
1
3
2
1
0
2
1
0
7
Page frames
Reference string
Virtual Memory
- LRU may require substantial hardware assistance
- The problem is to determine an order for the frames
defined by the time of last use

## Slide 8: Problems in Page Replacement
Consider a paging system in which M1 has a capacity of three pages. The execution of a program Q requires reference to five distinct pages Pi, where i= 1,2,3,4,5 and i is the page address. The page address stream formed by executing Q is
2 3 2 1 5 2 4 5 3 2 5 2

## Slide 9: Problem2
A virtual memory system has an address space of 8K words, a memory space of 4K words, and page and block sizes of 1K words. The following page reference chanses occur during a given time interval.
4 2 0 1 2 6 1 4 0 1 0 2 3 5 7
Determine the four pages that are resident in main memory after each page reference change if the replacement algorithm used is FIFO, LRU and OPT.

## Slide 10: Memory Portions
Key Characteristics – William Stallings
Main memory Organization (1-D,2-D,Static and dynamic RAM)–hayes[6], ppt, william Stallings.
Access methods – William Stallings
Design Problems – PPT, Morris Mano, Hayes
Memory Hierarchy – Morris Mano(12.1), Hayes (6.1)
Cache Memories –Morris Mano (12.5),PPT, William Stallings.
Virtual Memory and replacement Alg –Morris Mano (12.6)

## Slide 11: Unit –II reference Materials
Hardware and software implementation of arithmetic unit for common arithmetic operations: addition, subtraction, multiplication, division( Fixed point and floating point) = Refer Morris Mano chapter 10.
Data Representation = ppt.
Representation of non-numeric data (character codes, graphical data) = ppt, morris mano pg:383